## Slide 1: Differentiated Services
March 19, 1998
Gordon Chaffee
Berkeley Multimedia Research Center
University of California, Berkeley
Email: chaffee@bmrc.berkeley.edu
URL: http://bmrc.berkeley.edu/people/chaffee

## Slide 2: Outline
Architecture and goals
Service proposals
Extending to an end-to-end model
Notes: RSVP: The largest part of this talk will focus on RSVP and discuss what it is and how it works.
Emerging network protocols: In addition, I will briefly discuss other new network technologies such as IPV6, IP security, and Mobile iP.
Open Extensible Gateway: I’ll also talk a bit about the open extensible gateway and the issues involved in implementing one.
Testbed Network: Last, I am going to describe the network testbed that we are creating. We will use this network to run experiments with RSVP and gateways.

## Slide 3: Basic Ideas
Differentiated services provide a way to specify the relative priority of packets
Some data is more important than other data
People who pay for better service get it
Fujitsu Japan
Fujitsu of America
Limited Bandwidth
The real question is to choose which packets shall be dropped. The
first definition of differential service is something like "not mine.”
-- Christian Huitema

## Slide 4: Goals
Ability to charge differently for different services
Lightweight, scalable service discrimination suitable for network backbones
  No per flow state or per flow signaling
Deploy incrementally, then evolve
  Build simple system at first, expand if needed in future
Make service separate from signaling

## Slide 5: Comparison to Integrated Services
Must simpler than Integrated Services
No per flow state
No signaling protocol
Aggregates traffic into priority classes
No individual link resource allocations
Customer agreements are relatively static

## Slide 6: Architecture
All policy decisions made at network boundaries
  Boundary routers implement policy decisions by tagging packets with appropriate priority tag
  Traffic policing at network boundaries
No policy decisions within network
  Routers within network forward packets according to their priority tags

## Slide 7: Architecture Diagram
ISP 1
ISP 2
Backbone
Provider
Company A
Company B
Company C
Company D
Company E
Company F

## Slide 8: IP Priority
Must work with IPv4 and IPv6
  IPv4 has Type of Service (TOS) byte
  IPv6 has Class byte
Suggestions
  Define usage of the 8 bits
  Explicit congestion notification (1 or 2 bits)
  Various priority encoding schemes (1 - 3 bits)
  Leave some bits for future usage

## Slide 9: Issues
Configuration
Traffic behavior
Payments
Scope of service class
Security

## Slide 10: Configuration Discussion
Mostly static allocations initially
Service agreement
  Static agreements between customers and ISP
  Static agreements between ISPs
  Agent based (e.g. bandwidth brokers)
Scope of precedence
  Global: across all packets
  Local: restricted to packets belonging to an application, host, etc. (as in old IPv6 Class semantics)

## Slide 11: Traffic Behavior Discussion
Small percentage of traffic should be dedicated to premium services
Why?
  No explicit per link resource management
  Some links along popular pathways might be unable to meet their traffic guarantees
  When congestion occurs, more people likely to ask for premium service

## Slide 12: Payment Discussion
Who pays for service?
  Sender or receiver?
  Dependent on activity (e.g. 800 numbers for web)
  Problem with multicast
Dynamic payment schemes?

## Slide 13: Scope of Service Class
Packet priorities limited to an ISP
  Extend with bilateral ISP agreements
How can scope of priority be extended?
Differentiated services is unidirectional
Traffic marked for priority delivery
Traffic policed for profile violations
No marking of returning traffic

## Slide 14: Security Discussion
Security
  DS byte not covered by IPSEC authentication header
  Theft-of-service attack
  Need strong authentication for service authorization/configuration, policing at network boundary
Does diffserv increase the potential for misuse?

## Slide 15: Service Proposals
Proposed usage of Type of Service bits
Assured Service (1 bit)
Premium Service (1 bit)
Two-bit Differentiated Services

## Slide 16: Assured Service Dave Clark (MIT)
Statistically provisioned
  Provisioned according to expected capacity usage profiles
In profile traffic is “unlikely” to be dropped
Out of profile packets get best-effort delivery
Defines a better best-effort

## Slide 17: Assured Service Example
Assured Service
Drop if congested
Congested
Uncongested

## Slide 18: Premium Service Van Jacobson (LBL)
Conservative allocation of resources
  Provisioned according to peak capacity profiles
Shaped at boundaries to remove bursts
Out of profile packets dropped
Defines a virtual leased line: fixed maximum bandwidth, but available when needed

## Slide 19: Premium Service Example
Fixed Bandwidth
Drop always

## Slide 20: Two-bit Differentiated Services
Combines Assured and Premium Services
  Assured and Premium services use similar implementation mechanisms
  Premium service sets P-bit
  Assured service sets A-bit
Well defined building blocks to create a variety of services

## Slide 21: Two-Bit Border Router Functionality
Packet Input
Wait for token
Data Queue
Packet Output
Set
P-bit
Packet Input
Test if token
Packet Output
Set
A-bit
Data Queue
No token
Token
Premium Service
Assured Service
Token
Bucket
Token
Bucket

## Slide 22: Two-bit Internal Router Functionality
P-bit set?
Packets In
Low Priority Queue
High Priority Queue
If A-bit set,
a_cnt++
No
Yes
RED In/Out
Queue Management
If A-bit set,
a_cnt--
Packets Out

## Slide 23: Building Blocks
General classifier
  First hop router, at edges of network
Bit-pattern classifier
Bit setter
Priority queues
Shaping token buffer
Policing token bucket

## Slide 24: End-to-End Resource Allocation
Microsoft model
  Differentiated services in backbone
  RSVP in smaller networks
Bandwidth brokers
  Centralized control of bandwidth allocation within a domain
  Negotiate with other neighboring bandwidth brokers
Static allocations at first, but evolving toward dynamic allocations in time