## Slide 1: Virtual Private Networks (VPN) Network Address Translation (NAT)
March 19, 1998
Gordon Chaffee
Berkeley Multimedia Research Center
University of California, Berkeley
Email: chaffee@bmrc.berkeley.edu
URL: http://bmrc.berkeley.edu/people/chaffee

## Slide 2: Outline
Virtual Private Networks (VPNs)
  Desired Features
  Protocols
  Mobile IP
Network Address Translation (NAT)
  Basic Concepts
  Application Handling
  Multicast
Notes: RSVP: The largest part of this talk will focus on RSVP and discuss what it is and how it works.
Emerging network protocols: In addition, I will briefly discuss other new network technologies such as IPV6, IP security, and Mobile iP.
Open Extensible Gateway: I’ll also talk a bit about the open extensible gateway and the issues involved in implementing one.
Testbed Network: Last, I am going to describe the network testbed that we are creating. We will use this network to run experiments with RSVP and gateways.

## Slide 3: Introduction
All IP networks can be considered virtual networks
  Backbone networks run over ATM, Sonet, Frame Relay
  Local area networks run over Ethernet
Focus on running over IP networks

## Slide 4: Virtual Private Networks
Definition
  A VPN is a private network constructed within the public Internet
Goals
  Connect private networks using shared public infrastructure
  Simplify distributed network creation
Desirable properties
  Security
  Quality of service guarantees
Notes: The virtual private network model can provide for various functionality. A company may choose to setup a VPN to link up two remote sites into a single logical network. In this case, the VPN is a static entity. On the other hand, ISPs may use VPNs to provide virtual dialup functionality. Workers can dial into the ISP, and the ISP will setup a VPN to a company server. This allows the company to outsource its pool of modems to an organization that is better suited to providing dialup capabilities.
When dealing with non-IP protocols, this capability is even more important. Some of these protocols such as AppleTalk and IPX are not normally routable. The VPN allows these protocols to be carried through the virtual private network, allowing Macintoshes to see file shares from other Macintoshes.

## Slide 5: Motivations
Economic
  Using shared infrastructure lowers cost of networking
  Less of a need for leased line connections
Communications privacy
  Communications can be encrypted if required
  Ensure that third parties cannot use virtual network
Virtualized equipment locations
  ISPs, not businesses, build and administer modem pools
  Hosts on network do not need to be co-located

## Slide 6: VPN Features
Create logical network from multiple physical nets
Use unregistered IP addresses over Internet
Support multiple protocols
  Difficult to support AppleTalk, IPX across Internet

## Slide 7: Issues with VPNs
Quality of service
  Encapsulation can hide QoS markings
Security
  IP Security suggested for use with IP VPNs
Addressing
  Can two private networks with same IP address space be connected together by NAT translator?
  Can internal services be externally visible?
Notes: Performance guarantees are necessary for companies that want to reduce their dependence on SNA networks. SNA networks provide bandwidth guarantees, so having a way to replace these is important. One of the proposals for integrated services, originally from Van Jacobson, provides for a virtual circuit type connection. I will talk about that further in the Integrated Services talk.

## Slide 8: Configuration Questions
Application
Link
Layer
Network
Layer
Application
Link
Layer
Network Layer
Transport
Layer
Transport
Layer
What layer does a VPN encapsulate?
What layer does a VPN run across?

## Slide 9: Building a VPN
Controlled route propagation
  Only routers between VPN endpoints get routing tables
  BGP can provide multiple views of same network
Tunneling
Encryption

## Slide 10: Types of Service
Virtual dial-up
Wholesale dial-up
Logical network creation

## Slide 11: Virtual Dial-up Example (1)
Worker dials ISP to get basic IP service
Worker creates his own tunnel to Home Network
Internet
Tunnel
Gateway
Gateway
(NAS)
Internet Service Provider
Public Switched Telephone Network (PSTN)
Worker
Machine
Home Network

## Slide 12: Virtual Dial-up Example (2)
Remote worker connects to Home Network through ISP created tunnel
Allows wholesale dial-up
Internet
Tunnel
Gateway
(NAC)
Gateway
(NAS)
Internet Service Provider
Public Switched Telephone Network (PSTN)
Home Network

## Slide 13: Logical Network Creation Example
Remote networks 1 and 2 create a logical network
Secure communication at lowest level
Internet
Tunnel
Gateway
(NAC)
Gateway
(NAS)
Network 1
Network 2

## Slide 14: VPN Protocols
Point to Point Tunneling Protocol (PPTP)
  Microsoft, Ascend, others
Layer Two Forwarding (L2F)
  Cisco proposed
Layer Two Tunneling Protocol (L2TP)
  Unifies PPTP and L2P in single VPN standard

## Slide 15: PPTP
Protocol
  Data channel: PPP over IP GRE (Generic Routing Encapsulation)
  Encapsulates link layer (PPP), communicates at network layer (IP)
  Call setup handled in a control channel
Server in Windows NT 4.0
Clients for Win 95, NT 4.0

## Slide 16: PPTP Tunneling Example
ISP Gateway
PPTP Client Computer
PPTP Server Computer
PPP
Encapsulator
IP Packets
SMB Packets
PPTP
Interface
SLIP
Interface
PPP
Decapsulator
IP Packets
SMB Packets
PPTP
Interface
SLIP
Interface
IP Packets
IP GRE Packets

## Slide 17: PPTP Tunneling Example (cont’d)
PPTP
Interface
PPP
Encapsulator
SLIP
Interface
IP
Header
TCP
Header
Payload
Data
PPP
Header
IP GRE
Header
IP
Header
TCP
Header
Payload
Data
PPP
Header
IP
Header
TCP
Header
Payload
Data
IP
Header
TCP
Header
Payload
Data
PPP
Header
IP GRE
Header
SLIP
Header
TCP/IP Packet
Modem

## Slide 18: PPTP Problems
IP GRE is not handled by many firewalls

## Slide 19: L2TP
Virtual dial-up service
Requires no special software on a client
Standard PPP authentication
Enables services to work across Internet
  Unregistered IP addresses
  IPX, AppleTalk

## Slide 20: L2TP Protocol
Tunnel components
  Control channel
  Sessions for data delivery
Multiple tunnels may exist been LAC-LNS pair to support different QoS needs
Control
Session 1 (Call ID 1)
Session 2 (Call ID 2)
LAC
LNS
L2TP Access Concentrator
L2TP Network Server

## Slide 21: Control Channel
Functionality
  Setup, teardown tunnel
  Create, teardown payload “calls” within tunnel
  Keepalive mechanism to detect tunnel outages
Characteristics
  Retransmissions
  Explicit ACKs
  Sliding window congestion control
  In order delivery

## Slide 22: Sessions (Data Channels)
Payload delivery service
  Encapsulated PPP packets sent in sessions
  PPP over {IP, UDP, ATM, etc}
No fragmentation avoidance
Optional window based congestion control
Optional packet loss detection

## Slide 23: Security
Basic L2TP does not define security
PPP encryption can be used
IP Security encryption can be used
  L2TP extension to define security where IP Security is not available

## Slide 24: Mobile IP
Allows computer to roam and be reachable
Mobile IP vs DHCP/BOOTP
  Mobility vs Portability
Basic architecture
  Home agent (HA) on home network
  Foreign agent (FA) at remote network location
  Home and foreign agents tunnel traffic
  Non-optimal data flow
Notes: Reachable: want this if you have video/audio conferencing through the laptop.
Architecture: Draw a small picture of home agent, foreign agent, and the interaction.

## Slide 25: Mobile IP Example
Home
Agent
Foreign
Agent
Internet
Foreign Subnet
Home Subnet
Mobile Node
169.229.2.98
169.229.2.97
18.86.0.253
128.95.4.112
Fixed Node
Register
1. The Mobile Node registers itself with the Foreign Agent on the Foreign Subnet. The Foreign Agent opens an IP-IP tunnel to the Home Agent. The Home Agent begins listening for packets sent to 169.229.2.98.
2. The Fixed Node initiates a connection to the Mobile Node. It sends packets to the Mobile Node’s home IP address, 169.229.2.98. The packets are routed to the Home Subnet.
4. The Foreign Agent decapsulates the IP-IP packets, and it sends them out on the Foreign Subnet. These packets will be addressed to 169.229.2.98.
5. The Mobile Node receives the packets, and it sends responses directly to the Fixed Node at 128.95.4.112.
3. The Home Agent receives them, encapsulates them in IP-IP packets, and it sends them to the Foreign Agent. Encapsulated packets are addressed to 18.86.0.253.

## Slide 26: Dynamic DNS
Quick update times
Mobile hosts update name to IP address mapping as they move around.
Problem
  Moving between cells or networks causes IP addresses to change
  TCP connections require constant IP addresses
Works for occasionally mobile hosts

## Slide 27: Network Address Translation

## Slide 28: Background
IP defines private intranet address ranges
  10.0.0.0 - 10.255.255.255 (Class A)
  172.16.0.0 - 172.31.255.255 (Class B)
  192.168.0.0 - 192.168.255.255 (Class C)
Addresses reused by many organizations
Addresses cannot be used for communication on Internet

## Slide 29: Problem Discussion
Hosts on private IP networks need to access public Internet
All traffic travels through a gateway to/from public Internet
Traffic needs to use IP address of gateway
Conserves IPv4 address space
  Private IP addresses mapped into fewer public IP addresses

## Slide 30: Scenario
Gateway
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
Host A
BMRC
Server
24.1.70.210
128.32.32.68
All Private Network hosts must use the gateway IP address
Private Network
Public Internet
Public network IP address, globally unique
Same private network IP addresses may be used by many organizations

## Slide 31: Simple Example
Gateway
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
Host A
BMRC
Server
24.1.70.210
128.32.32.68
Private Network
Public Internet

## Slide 32: Possible Solutions
Proxy servers run on gateway
  TCP level
Translate IP addresses in data streams
  IP level solution

## Slide 33: Proxy Server Solution
Client programs use special protocol to communicate with proxy server
  SOCKS
Proxy servers are protocol specific
  HTTP, HTTPS, FTP
  UDP based protocols are more difficult to forward
Provides good site security
  Protocols must be explicitly setup to pass through gateway
  New protocols will not pass by default

## Slide 34: Proxy Server Example
Gateway
TCP Connection 1
Server
FTP
Proxy
HTTP
Proxy
HTTPS
Proxy
SOCKS
Server
128.32.32.68
bmrc.berkeley.edu
“Open http://bmrc.berkeley.edu”
TCP Connection 2

## Slide 35: Network Address Translation Solution
Special function on gateway
  IP source and destination addresses are translated
  Internal hosts need no changes
No changes required to applications
TCP based protocols work well
Non-TCP based protocols more difficult
Provides some security
  Hosts behind gateway difficult to reach
  Possibly vulnerable to IP level attacks

## Slide 36: NAT Example
NAT Gateway
Server
Address
Translator
128.32.32.68
bmrc.berkeley.edu
TCP Connection 1
TCP Connection 1

## Slide 37: Load Balancing Servers with NAT
Single IP address for web server
Redirects workload to multiple internal servers
Server
Server
Server
Server
NAT
Gateway
(Virtual
Server)
Private
Intranet
Public
Internet

## Slide 38: Load Balancing Networks with NAT
NAT
Gateway
Connections from Private Intranet split across Service Providers 1 and 2
Load balances at connection level
  Load balancing at IP level can cause low TCP throughput
Private
Intranet
Service Provider 1
Service Provider 2
Network X

## Slide 39: NAT Discussion
NAT works best with TCP connections
NAT breaks End-to-End Principle by modifying packets
Problems
  Applications use IP addresses within data stream (FTP)
  Connectionless UDP (Real Audio, CU-SeeMe)
  ICMP (Ping)
  Multicast
Need to watch/modify data packets
Notes: NAT works bets with applications that make connections to the outside world using TCP connections. It has trouble with datagram protocols.

## Slide 40: TCP Protocol Diagram
Client
Server
SYN, ACK
Packet 0:50
ACK 0:50
FIN
FIN, ACK
Source IP Address
Destination IP Address
Checksum
Sequence Number
Dest Port Number
Source Port Number
TCP Header
. . . . .
. . . . .
IP Header
. . . . .
ACK
SYN
SYN flag indicates a new TCP connection

## Slide 41: TCP NAT Example
Server
Internet
10.0.0.3
24.1.70.210
128.32.32.68
NAT
Gateway
PROTO
SADDR
DADDR
SPORT
DPORT
FLAGS
CKSUM
TCP
24.1.70.210
128.32.32.68
40960
80
SYN
0x2436
2
2. NAT gateway sees SYN flag set, adds new entry to its translation table. It then rewrites the packet using gateway’s external IP address, 24.1.70.210. Updates the packet checksum.
10.0.0.1
PROTO
SADDR
DADDR
SPORT
DPORT
FLAGS
CKSUM
TCP
128.32.32.68
24.1.70.210
80
40960
SYN, ACK
0x8041
3
3. Server responds to SYN packet with a SYN,ACK packet. The packet is sent to the NAT gateway’s IP address.
Client Server
IPAddr Port IPAddr Port NATPort
10.0.0.3 1049 128.32.32.68 80 40960
. . . .. . . . .. . .
NAT Translation Table
PROTO
SADDR
DADDR
SPORT
DPORT
FLAGS
CKSUM
TCP
10.0.0.3
128.32.32.68
1049
80
SYN
0x1636
1
1. Host tries to connect to web server at 128.32.32.68. It sends out a SYN packet using its internal IP address, 10.0.0.3.
PROTO
SADDR
DADDR
SPORT
DPORT
FLAGS
CKSUM
TCP
128.32.32.68
10.0.0.3
80
1049
SYN, ACK
0x7841
4
4. NAT gateway looks in its translation table, finds a match for the source and destination addresses and ports, and rewrites the packet using the internal IP address.

## Slide 42: Example: FTP
13:34:53.565221 home.2145 > roger-rabbit.ftp: P 40:63(23) ack 236 win 32120 (DF) [tos 0x10]
4510 003f a76c 4000 4006 9405 1801 46d2 E..?.l@.@.....F.
8020 2044 0861 0015 c58b 827a 241d c60c . D.a.....z$...
5018 7d78 a120 0000 504f 5254 2032 342c P.}x. ..PORT 24,
312c 3730 2c32 3130 2c38 2c39 380d 0a 1,70,210,8,98..
FTP client sends PORT command: IP address and port number (24.1.70.210: 2146) that FTP server can open a connection to.
13:34:53.605971 roger-rabbit.ftp > home.2145: P 236:266(30) ack 63 win 31744 (DF) [tos 0x10]
4510 0046 672e 4000 3406 e03c 8020 2044 E..Fg.@.4..<. D
1801 46d2 0015 0861 241d c60c c58b 8291 ..F....a$.......
5018 7c00 3cd2 0000 3230 3020 504f 5254 P.|.<...200 PORT
2063 6f6d 6d61 6e64 2073 7563 6365 7373 command success
6675 6c2e 0d0a ful...
Client sends LIST command to get a directory listing from the FTP server.
13:34:53.606640 home.2145 > roger-rabbit.ftp: P 63:69(6) ack 266 win 32120 (DF) [tos 0x10]
4510 002e a76e 4000 4006 9414 1801 46d2 E....n@.@.....F.
8020 2044 0861 0015 c58b 8291 241d c62a . D.a......$..*
5018 7d78 4b94 0000 4c49 5354 0d0a P.}xK...LIST..
FTP server opens a data channel (SYN) to client port 2146, and the client accepts the connection.
13:34:53.645008 roger-rabbit.20 > home.2146: S 2732123529:2732123529(0) win 512 mss 1460> [tos 0x8]
13:34:53.645173 home.2146 > roger-rabbit.20: S 3319148401:3319148401(0) ack 2732 123530 win 32120 <mss 1460> (DF)
13:34:53.655651 roger-rabbit.ftp > home.2145: . ack 69 win 31744 (DF) [tos 0x10]
13:34:56.761633 roger-rabbit.20 > home.2146: . ack 1 win 31744 (DF) [tos 0x8]
13:34:56.761977 roger-rabbit.ftp > home.2145: P 266:319(53) ack 69 win 31744 (DF) [tos 0x10]
4510 005d 68be 4000 3406 de95 8020 2044 E..]h.@.4.... D
1801 46d2 0015 0861 241d c62a c58b 8297 ..F....a$..*....
5018 7c00 4ff7 0000 3135 3020 4f70 656e P.|.O...150 Open
696e 6720 4153 4349 4920 6d6f 6465 2064 ing ASCII mode d
6174 6120 636f 6e6e 6563 7469 6f6e 2066 ata connection f
6f72 202f 6269 6e2f 6c73 2e0d 0a or /bin/ls...
Beginning of directory listing on data channel.
13:34:56.765356 roger-rabbit.20 > home.2146: P 1:432(431) ack 1 win 31744 (DF) [tos 0x8]
4508 01d7 68bf 4000 3406 dd22 8020 2044 E...h.@.4..". D
1801 46d2 0014 0862 a2d8 e58a c5d6 2f72 ..F....b....../r
5018 7c00 4a9a 0000 746f 7461 6c20 370d P.|.J...total 7.
0a64 7277 7872 7778 722d 7820 2020 3720 .drwxrwxr-x 7
6173 7761 6e20 2020 2070 6c61 7465 6175 aswan plateau
2020 2020 2020 3130 3234 204d 6172 2032 1024 Mar 2
3720 2031 3939 3720 2e0d 0a64 7277 7872 7 1997 ...drwxr
7778 722d 7820 2020 3720 6173 7761 6e20 wxr-x 7 aswan
2020 2070 6c61 7465 plate
13:34:56.765438 roger-rabbit.20 > home.2146: F 432:432(0) ack 1 win 31744 [tos 0x8]

## Slide 43: Example: Ping (ICMP)
ICMP Echo(8) or Echo Reply(0)
IP Header
Source IP Address
Destination IP Address
Header Checksum
ICMP
Length
Checksum
Type = 8 or 0
Code = 0
Sequence Number
Identifier = 0x1e0e
Optional Data
In ICMP Echo packet, NAT gateway sets Identifier to unique ID. The unique ID is used to find the original Source IP Address for an Echo Reply packet.
NAT gateway changes Source IP address to external NAT gateway address. It also updates the two checksums.

## Slide 44: NAT and Multicast Outline
Single interior network
  Examples
  Rules
Multiple interior networks
  Examples
  Rules

## Slide 45
NAT
Gateway
Multicast
Router
Private Network
Single Interior Network Diagram
Host

## Slide 46: Example: Joining a Multicast Group
NAT
Gateway
Multicast
Router
Private Network
Membership
Report
Membership
Report
The NAT gateway changes the source address in the IGMP Membership Report, then forwards the message onto the external network.
Host

## Slide 47: Example: Multicast Membership Queries
NAT
Gateway
Multicast
Router
Private Network
2. NAT gateway forwards the IGMP Membership Query onto the Private Network with no modifications.
Membership Query
Membership
Report
4. The NAT gateway changes the source address in the IGMP Membership Report, then forwards the message onto the external network.
Membership Query
Host
Membership
Report
3. After a random delay, the host responds with a Membership Report message
Membership Query
1. Multicast Router sends a Membership Query message to its attached network.

## Slide 48: NAT: No Internal Multicast Routers
Simple header processing rules
  In => Out: Source address => NAT gateway address
  Out => In: No changes necessary
Application issues
  RTP reports use unique names based on IP addresses
    Use chaffee_10.0.0.3@24.1.70.210
  SDP announcements include IP addresses
Data filtering required for some applications

## Slide 49: Multiple Interior Networks Diagram
NAT
Gateway
Interior
MRouter
Exterior
Multicast
Router
Private Network
The NAT Gateway acts as a simple host on Network 1, but it acts as an Interior Multicast Router in the Private Network.
Interior
Multicast
Router
Network 1 (Leaf Network)
Network 2
Network 3

## Slide 50: NAT with Interior Multicast Routers
Requirements
  Need multicast routing if there are multiple internal networks
  NAT gateway cannot advertise routes to Internet
  NAT gateway must appear only as a host to external multicast router

## Slide 51: NAT with Interior Multicast Routers
NAT gateway must appear as a host to external multicast router
DVMRP
  Uses data flooding and pruning to build multicast trees
  Internal source causes trouble
  Exterior multicast router does not send prune messages onto leaf networks, so internal source is not pruned
  Traffic from source always flows to NAT gateway
  Therefore, NAT gateway should run DVMRP internally
Explicit joins work better (e.g. CBT, PIM)

## Slide 52: DVMRP on External Network
Multicast
Router C
Multicast
Router B
Multicast
Router D
Network 1 (Leaf Network)
Network 2
Network 3
Sender A (225.1.1.1)
{A,225.1.1.1}: if=1, of=2
1
2
{A,225.1.1.1}: if=2, of=1
2
1
{A,225.1.1.1}: if=2, of=1(leaf)
2
1
Receiver
Membership
Report
Receiver joins multicast group 225.1.1.1
Membership
Query
Membership
Report
Membership
Query
Membership
Query

## Slide 53: DVMRP on NAT Network
NAT
Gateway
Interior
MRouter
Exterior
Multicast
Router
Private Network
Interior
Multicast
Router
Network 1 (Leaf Network)
Network 2
Network 3
Sender A (225.1.1.1)
{A,225.1.1.1}: if=1, of=2(leaf)
1
2
Membership
Query
Receiver
Receiver joins multicast group 225.1.1.1
Membership
Report
2
1
2
1
Membership
Report
Membership
Query
Membership
Report

## Slide 54: DVMRP on NAT Network (Prunes)

## Slide 55: PIM Background
Shared tree for each multicast group, source specific bypasses
Rendezvous Point (RP) is the root of the shared tree
All Join/Prune messages of form {*,G} sent to RP
All multicast data travels through RP

## Slide 56: PIM on NAT Network: Joining a Group
NAT
Gateway
RP, Interior
PIM Router
Exterior
Multicast
Router
Private Network
Membership
Query
Membership
Report
The NAT gateway needs to be the RP for all groups that are not administratively scoped.
Interior
PIM
Router
Network 1
Receiver joins multicast group 225.1.1.1
Membership
Report
Sender A
(225.1.1.1)
1
2
2
1
2
1
Join
{A,225.1.1.1}: if=2, of=1(leaf)
{A,225.1.1.1}: if=2, of=1
Membership
Report
{A,225.1.1.1}: if=1, of=2(leaf)

## Slide 57: PIM on NAT Network
NAT gateway must be the Rendezvous Point for all multicast groups that are not locally scoped
PIM semantics for PIM Border Multicast Routers (PBMRs) are not rich enough for RP to be elsewhere