## Slide 1: IP Multicast/Multicast Routing
March 19, 1998
Gordon Chaffee
Berkeley Multimedia Research Center
University of California, Berkeley
Email: chaffee@bmrc.berkeley.edu
URL: http://bmrc.berkeley.edu/people/chaffee

## Slide 2: Outline
IP Multicast
Basic routing
  Distance Vector Routing
  Path Vector Routing
Multicast routing
  Design choices
  Distance Vector Multicast Routing Protocol (DVMRP)
  Core Based Trees (CBT)
  Protocol Independent Multicast (PIM)
  Border Gateway Multicast Protocol (BGMP)
Multicast address allocation

## Slide 3: Commercial Motivation
Problem
  Traffic on Internet is growing about 100% per year
  Router technology is getting better at 70% per year
  Routers that are fast enough are very expensive
ISPs need to find ways to reduce traffic

## Slide 4: Unicast
R
Sender
Problem
  Sending same data to many receivers via unicast is inefficient
Example
  Popular WWW sites become serious bottlenecks

## Slide 5: Multicast
R
Sender
Efficient one to many data distribution

## Slide 6: Commercial Interest
Software distribution
WWW: Distribute data from popular sites to caches throughout Internet
Send video/audio streams multicast
  Disney experiment
But...
  ISPs do not know how multicast will affect revenues
  Want to limit who can send multicast data

## Slide 7: Multicast
History
  Long history of usage on shared medium networks
  Data distribution
  Resource discovery: ARP, Bootp, DHCP
Ethernet
  Broadcast (software filtered)
  Multicast (hardware filtered)
Multiple LAN multicast protocols
  DECnet, AppleTalk, IP
Notes: Multicast has been used on shared medium networks for many years. This includes ethernet and satellite links. Satellite television services are good examples of the use of multicast--one program is sent, and people over a distributed geographic range can all listen to the same show.

## Slide 8: IP Multicast Introduction
Efficient one to many data distribution
  Tree style data distribution
  Packets traverse network links only once
Location independent addressing
  IP address per multicast group
Receiver oriented service model
  Applications can join and leave multicast groups
  Senders do not know who is listening
  Similar to television model
  Contrasts with telephone network, ATM
Notes: Scales to an arbitrary number of sites. No problems with setup time.

## Slide 9: IP Multicast
Service
  All senders send at the same time to the same group
  Receivers subscribe to any group
  Routers find receivers
Unreliable delivery
Reserved IP addresses
  224.0.0.0 to 239.255.255.255 reserved for multicast
  Static addresses for popular services (e.g. SAP)
Notes: N to N service model. Everyone receives everyone else's traffic. This is much like a CB radio scheme. Each sender is like a television station sending to a set of receivers.
Packets are only sent to interested receivers.
Some of the 224.0.0.x addresses are used by IP routing algorithms.

## Slide 10: Internet Group Management Protocol (IGMP)
Protocol for managing group membership
  IP hosts report multicast group memberships to neighboring routers
  Messages in IGMPv2 (RFC 2236)
    Membership Query (from routers)
    Membership Report (from hosts)
    Leave Group (from hosts)
Announce-Listen protocol with Suppression
  Hosts respond only if no other hosts has responded
Soft State protocol
Notes: IGMP is one of a series of Announce-Listen protocols. We will again see this method used in later protocols such as RTCP, SRM, and SCUBA.
The low volume of traffic is achieved by avoiding duplicated messages where possible.

## Slide 11: IGMP Example (1)
Network 1
Host 1 begins sending packets
  No IGMP messages sent
  Packets remain on Network 1
Router periodically sends IGMP Membership Query
Network 2
Router
1
2
4
3

## Slide 12: IGMP Example (2)
Network 1
Host 3 joins conference
  Sends IGMP Membership Report message
Router begins forwarding packets onto Network 2
Host 3 leaves conference
  Sends IGMP Leave Group message
  Only sent if it was the last host to send an IGMP Membership Report message
Network 2
Router
1
2
4
3
3
Membership Report
3
3
Leave Group

## Slide 13: Source Specific Filtering: IGMPv3
Adds Source Filtering to group selection
  Receive packets only from specific source addresses
  Receive packets from all but specific source addresses
Benefits
  Helps prevent denial of service attacks
  Better use of bandwidth
Status: Currently an Internet Draft

## Slide 14: IGMPv3 Source Filtering (1)
Senders 1, 2, and 3 are sending to the same multicast group.
The receiver sent an IGMPv3 Group-and-Source-Specific message to join the multicast group but to exclude all traffic from Sender 1.
R1
R3
R4
Sender 1
Sender 3
Receiver
Sender 2
R2
If using an IGMPv2 join, router R1 would forward traffic from all senders to router R4. However, in this case with IGMPv3, no traffic from Sender 1 is forwarded to router R4.

## Slide 15: IGMPv3 Source Filtering (2)
R1
R3
R4
Sender 1
Sender 3
Receiver
Senders 1, 2, and 3 are sending to the same multicast group.
The Receiver sent an IGMPv3 Group-and-Source Specific message to join the multicast group and receive traffic from only Sender 3.
Sender 2
R2
In an IGMPv2 join, routers R1, R2, and R3 would forward traffic. In the case of IGMPv3, only router R3 forwards traffic to router R4.

## Slide 16: Scoping Multicast Traffic
TTL based
  Based on Time to Live (TTL) field in IP header
  Only packets with a TTL > threshold cross boundary
Administrative scoping
  Set of addresses is not forwarded past domain
  More flexible than TTL based.
Scoped addresses
  224.0.0.* never leaves subnet

## Slide 17: TTL Scoping Example
R1
R3
Receiver 3
Receiver 1
Sender
R2
Receiver 2
Network 1
Network 2
Network 3
Network 4
TTL=1
TTL=2
TTL=3
R4
TTL=4
TTL=4
TTL=33
R4 blocks traffic
with TTL < 32

## Slide 18: Administrative Scoping Example
R1
R2
R3
R4
Host
CAIRN High Speed Network
UC Berkeley Network
To Rest
of World
To Rest
of World
Administrative scoping allows traffic to be limited to a region based on its multicast group address, resulting in more flexible network configurations.
The Host can send traffic that is limited to only the CAIRN High Speed Network, to only the UC Berkeley Network, to both, or to the rest of the world.
239.2.0.0 - 239.2.255.255: Traffic scoped to only the CAIRN High Speed Network
239.3.0.0 - 239.3.255.255: Traffic scoped to only the UC Berkeley Network
239.4.0.0 - 239.4.255.255: Traffic scoped to both the CAIRN and UC Berkeley Networks
224.0.1.0 - 238.255.255.255: Traffic scoped to the rest of the world

## Slide 19: Distance Vector Routing
First decentralized IP routing algorithm
Building routing tables
  Begin with routers knowing only local links and distance to self
  Neighbor routers exchange current distance vectors
  New distances computed using neighbors’ distance vectors
Routing tables
  Nodes maintain distance from self to every destination

## Slide 20: Distance Vector Example
A
B
D
E
C
1. Begin with all distance vectors only knowing
distance to self. Assume link costs are 1.
2. Initial distance vectors are sent to neighbors,
and nodes compute new distance vectors.
3. Send distance vectors; nodes re-compute vectors.
L1
L3
L2
L4
L5
A
A 0 XX
B
B 0 XX
C
C 0 XX
D
D 0 XX
E
E 0 XX
E
E 0 XX
D 1 L4
C 1 L5
A
A 0 XX
B 1 L1
D 1 L3
B
B 0 XX
A 1 L1
C 1 L2
C
C 0 XX
B 1 L2
E 1 L5
D
D 0 XX
A 1 L3
E 1 L4
A
A 0 XX
B 1 L1
D 1 L3
C 2 L1
E 2 L3
B
B 0 XX
A 1 L1
C 1 L2
D 2 L1
E 2 L2
C
C 0 XX
B 1 L2
E 1 L5
A 2 L2
D 2 L5
D
D 0 XX
A 1 L3
E 1 L4
B 2 L3
C 2 L4
E
E 0 XX
D 1 L4
C 1 L5
A 2 L4
B 2 L5
4. Now, the network has converged. No changes will
occur in the distance vectors without a topology
change.
* Note: Routing updates sent at random intervals, not synchronously as shown in this example.
Notes: Talk about case of L2 going down. Then talk about case
of C going down.

## Slide 21: Distance Vector Problems
Problems
  Routing tables slow to converge
  Route flapping
  Cycles can occur after topology changes
Optimizations
  Triggered updates
  Split horizon with poison reverse
A
B
C
L1
L2
Cycle in tables

## Slide 22: Distance Vector Example 2
A
B
D
E
C
L1
L3
L2
L4
L5
A
A 0 XX
B 1 L1
D 1 L3
C 2 L1
E 2 L3
B
B 0 XX
A 1 L1
C 1 L2
D 2 L1
E 2 L2
C
C 0 XX
B 1 L2
E 1 L5
A 2 L2
D 2 L5
D
D 0 XX
A 1 L3
E 1 L4
B 2 L3
C 2 L4
E
E 0 XX
D 1 L4
C 1 L5
A 2 L4
B 2 L5
1. Begin with the converged routing tables from the previous example.
2. Link L2 between B and C fails. B begins using link L1 to get to C. However, A uses link L1 to get to C, so there is now a cycle between A and B. There is also a cycle between C and E.
A
A 0 XX
B 1 L1
D 1 L3
C 2 L1
E 2 L3
B
B 0 XX
A 1 L1
C 3 L1
D 2 L1
E 2 L2
C
C 0 XX
B 3 L5
E 1 L5
A 2 L2
D 2 L5
D
D 0 XX
A 1 L3
E 1 L4
B 2 L3
C 2 L4
E
E 0 XX
D 1 L4
C 1 L5
A 2 L4
B 2 L5
Temporary Cycle
3. Routing tables continue to be exchanged.
A
A 0 XX
B 1 L1
D 1 L3
C 3 L3
E 2 L3
B
B 0 XX
A 1 L1
C 3 L1
D 2 L1
E 2 L2
C
C 0 XX
B 3 L5
E 1 L5
A 2 L2
D 2 L5
D
D 0 XX
A 1 L3
E 1 L4
B 2 L3
C 2 L4
E
E 0 XX
D 1 L4
C 1 L5
A 2 L4
B 3 L4
4. Routing tables converge after another exchange.
A
A 0 XX
B 1 L1
D 1 L3
C 3 L3
E 2 L3
B
B 0 XX
A 1 L1
C 4 L1
D 2 L1
E 2 L2
C
C 0 XX
B 4 L5
E 1 L5
A 2 L2
D 2 L5
D
D 0 XX
A 1 L3
E 1 L4
B 2 L3
C 2 L4
E
E 0 XX
D 1 L4
C 1 L5
A 2 L4
B 3 L4

## Slide 23: Path Vector Routing
Distribute full paths to destinations
Simple
Converges quickly
Every node on network knows full network topology
Used by the Border Gateway Protocol (BGP)

## Slide 24: Multicast Routing Discussion
What is the problem?
  Need to find all receivers in a multicast group
  Need to create spanning tree of receivers
Design goals
  Minimize unwanted traffic
  Minimize router state
  Scalability
  Reliability

## Slide 25: Tree Building Choices
Flood and prune
  Distance Vector Multicast Routing Protocol (DVMRP)
  Protocol Independent Multicast Dense Mode (PIM-DM)
Explicit join
  Core Based Trees (CBT)
  Protocol Independent Multicast Sparse Mode (PIM-SM)
Flood network topology to all routers
  Link state protocol
  MOSPF

## Slide 26: Data Flooding
Send data to all nodes in network
Problem
  Need to prevent cycles
  Need to send only once to all nodes in network
  Could keep track of every packet and check if it had previously visited node, but means too much state
Sender
R3
R1
R2

## Slide 27: Reverse Path Forwarding (RPF)
Simple technique for building trees
Send out all interfaces except the one with the shortest path to the sender
In unicast routing, routers send to the destination via the shortest path
In multicast routing, routers send away from the shortest path to the sender

## Slide 28: Reverse Path Forwarding Example
R5
R6
R3
R2
R1
R4
R7
Sender
2. Router R2 accepts packets sent from Router R1 because that is the shortest path to the Sender. The packet gets sent out all interfaces.
1. Router R1 checks: Did the data packet arrive on the interface with the shortest path to the Sender? Yes, so it accepts the packet, duplicates it, and forwards the packet out all other interfaces except the interface that is the shortest path to the sender (i.e the interface the packet arrived on).
Drop
Drop
3. Router R2 drops packets that arrive from Router R3 because that is not the shortest path to the sender. Avoids cycles.

## Slide 29: Data Distribution Choices
Source rooted trees
  State in routers for each sender
  Forms shortest path tree from each sender to receivers
  Minimal delays from sources to destinations
Shared trees
  All senders use the same distribution tree
  State in routers only for wanted groups
  No per sender state (until IGMPv3)
  Greater latency for data distribution

## Slide 30: Source Rooted vs Shared Trees
B
A
C
D
B
A
C
D
Source Rooted Trees
Shared Tree
Traffic is heavily concentrated on some links while others get little utilization.
Routers maintain state for each sender in a group.
Often does not use optimal path from source to destination.

## Slide 31: Distance Vector Multicast Routing (DVMRP)
Steve Deering, 1988
Source rooted spanning trees
  Shortest path tree
  Minimal hops (latency) from source to receivers
Extends basic distance vector routing
Flood and prune algorithm
  Initial data sent to all nodes in network using RPF
  Prunes remove unwanted branches
  State in routers for all unwanted groups
  Periodic flooding since prune state times out (soft state)
Notes: DVMRP is an extension to the basic distance vector routing algorithm we looked at earlier. Steve Deering first published this work in 1988, and he refined it over the next few years. We will look at the basics of DVMRP, and then we will take a closer look at it.
DVMRP builds a source routed tree. The reason to use a source routed spanning tree is that is uses the shortest path distribution tree from the sender to each destination. This means delays will be minimal. This does not mean the tree has the lowest overall network cost.
How do you find the shortest path from a source to a destination?
How does DVMRP build the source routed trees? How does it find all the receivers in a network? It uses a flood and prune algorithm. When a sender first sends data to a new multicast group, the data is broadcast to all nodes in the network. Routers in the network with no downstream receivers remove themselves from the distribution tree by sending prune messages to upstream routers. Periodically, this prune times out, and data will once again flood through the router until it once again gets pruned back.

## Slide 32: DVMRP Algorithm
Truncated Reverse Path Multicast
  Optimized version of Reverse Path Forwarding
  Truncating
    No packets sent onto leaf networks with no receivers
Pruning
  Prune messages sent if no downstream receivers
  State maintained for each unwanted group
Grafting
  On join or graft, remove prune state and propagate graft message

## Slide 33: Truncated Reverse Path Multicast Example
R5
R6
R3
R2
R1
R4
R7
Sender
Router R2 accepts packets sent from Router R1 because that is the shortest path to the Sender.
Unlike Reverse Path Forwarding, which simply forwards out all but the incoming interface, DVMRP’s Reverse Path Multicast maintains a list of child links for each sender. It sends packets only out child links, not parent or sibling links. This means Router R2 will not forward data from the Sender to Router R3.
Siblings
Receiver
Truncation: no packets forwarded onto leaf networks with no receivers

## Slide 34: DVMRP Pruning Example
R5
R6
R3
R2
R1
R4
R7
Sender
Receiver
Prune
Prune
Prune
Prune

## Slide 35: DVMRP Grafting Example
R5
R6
R3
R2
R1
R4
R7
Sender
Receiver 1
Membership
Report
Receiver 2
Receiver 2 joins multicast group
Join from Receiver 2 causes router to remove its prune state and send a Join message up toward the Sender.
Graft
Prune State
Graft

## Slide 36: Multicast Tunneling
Problem
  Not all routers are multicast capable
  Want to connect domains with non-multicast routers between them
Solution
  Encapsulate multicast packets in unicast packet
  Tunnel multicast traffic across non-multicast routers
MBONE
  Multicast capable virtual network, subset of Internet
  Native multicast regions connection with tunnels
Notes: Because the routing tables is created independently of the unicast routing tables, tunnels are easier to deal with in DVMRP than in routing protocols that use the unicast routing tables.

## Slide 37: Multicast Tunneling Example (1)
UR1
UR2
Multicast
Router 1
Multicast
Router 2
Sender 1
Encapsulated
Data Packet
Unicast Routers
Multicast Router 1 encapsulates multicast packets for groups that have receivers outside of network 1. It encapsulates them as unicast IP-in-IP packets.
Network 1
Receiver
Network 2
Multicast Router 2 decapsulates IP-in-IP packets. It then forwards them using Reverse Path Multicast.

## Slide 38: Multicast Tunneling Example (2)
MR1
MR2
Virtual
Interfaces
Virtual Network Topology

## Slide 39: DVMRP Problems
Problems of distance vector routing
State maintained for unwanted groups
Bandwidth intensive
  Periodic data flooding per group
    No explicit joins, and prune state times out
  Not suitable for heterogeneous networks
Poorly handles large number of senders
  Scaling = O(Senders, Groups)

## Slide 40: Multicast Problems
Debugging is difficult
Immature protocols and applications
Interoperability
  Flood and prune/explicit join
Routing instability
Multicast breaks telco/ISP traffic charging and management models
Notes: It is easy to misconfigure a multicast router, and then it will inject copies of routes into the network. This is usually caused by interoperability issues with PIM and DVMRP.

## Slide 41: Operational Problems
Debugging is difficult
Misconfigured routers inject unicast routing tables into multicast routing tables
Black holes
  Cisco to Cisco tunneling using DVMRP doesn’t work
    Routes exchanged, but no data flows
  RPF checks on different routers think multicast traffic should be coming from the other router
Backchannel tunnels
  Improper tunnels cause non-optimal routing behavior

## Slide 42: Backchannel Tunneling
University of Illinois
UC Berkeley
Cornell University
ISP 1
ISP 2
BBN
A
B
Y
Z
X
X
Z
UC Berk
Cornell
Univ
ISP 2
Univ of
Illinois
B
Physical Network
Virtual Network
Backchannel
Tunnel from
X to Z
Backchannel tunnel causes B to send multicast traffic to X through Z. This is bad for the network.
ISP 1

## Slide 43: Debugging Multicast Problems
Local LAN debugging
  tcpdump
    tcpdump ip multicast
    tcpdump igmp
Routing debugging
  mrinfo
  mstat
  mtrace

## Slide 44: Core Based Trees (CBT)
Attributes
  Single shared tree per group => sparse trees
  Large number of senders
  Routing tables scale well, size = O(Groups)
  Bi-directional tree

## Slide 45: Group Management in CBT
R1
R
R2
R3
R
R
R
Receiver 1
Join
Join
Join
1. Receiver 1 joins the multicast group, causing Router R2 to join the shared tree by sending a Join message toward the Core. The Core sends an explicit ACK back to to Router R2.
R
R4
R
Core
Receiver 2
Ack
Ack
Ack
Join
Ack
2. Receiver 2 also joins the multicast group, causing Router R3 to join the shared tree by sending a Join message toward the Core. Router R4 is already part of the shared tree, so it adds R3 to the shared tree and sends back an ACK.

## Slide 46: Sending Data in CBT (1)
R1
R
R2
R3
R
R
R
Receiver 1
Packets from the Sender are propagated by routers on the shared tree by sending out all interfaces that are branches of the tree except the interface the packet arrived on.
R5
R4
R
Core
Receiver 2
Sender
Case 1: Sender is a member of the multicast group, and the first hop router is on the shared tree.

## Slide 47: Sending Data in CBT (2)
R1
R
R2
R3
R
R
R
Receiver
1. Router R1 is not on the shared tree, so it does an IP-in-IP encapsulation of packets from the Sender, and it unicasts the encapsulated packets to the Core.
R5
R4
R
Core
Receiver
Receiver
Case 2: Sender is not a member of the multicast group, and the first hop router is not on the shared tree.
Sender
Encapsulated
Data Packet
2. The Core decapsulates the encapsulated packets, and it distributes them out the shared tree.
Notes: When a receiver leaves a tree and there are no additional downstream routers, the router sends a QUIT_NOTIFICATION message to its parent router. There is no acknowledgement of this message.
If a router ever loses connectivity to its parent, it sends a FLUSH_TREE message downstream.

## Slide 48: Protocol Independent Multicast (PIM)
Uses unicast routing table for topology
Dense mode (PIM-DM)
  For groups with many receivers in local/global region
  Like DVMRP, a flood and prune algorithm
Sparse mode (PIM-SM)
  For groups with few widely distributed receivers
  Builds shared tree per group, but may construct source rooted tree for efficiency
  Explicit join

## Slide 49: PIM Sparse Mode
Hybrid protocol that combines features of DVMRP and CBT
Suited to widely distributed, heterogeneous networks
Shared tree centered at Rendezvous Point (RP)
Shared tree introduces sources to receivers
Source specific trees for heavy traffic flows
Unidirectional distribution tree

## Slide 50: Group Management in PIM-SM
DR1
R
DR2
R
R
R
R
Receiver 1
Rendezvous Point
1. Receiver 1 joins the multicast group. Designated Router DR2 sends a Join message toward the RP. Periodically, DR2 resends the Join message in case it was lost.
Join
Join
Join
2. Routers along the path to RP create router state for the group, adding themselves to the shared tree.
R
R
R
RP
Join
Join
Join
Notes: Actual message is a Join/Prune:
Multicast-Address = G
Join = {RP, WC-bit, RPT-bit}
WC-bit = Wildcard bit
RPT-bit = Rendezvous point tree bit
Prune = NULL
DR = Designated Router

## Slide 51: Sending Data in PIM-SM
DR1
R
DR2
R
R
Receiver 1
Rendezvous Point (RP)
1. Sender 1 begins sending to a multicast group.
2. Designated Router DR1 encapsulates the packets from Sender 1 in Register messages and unicasts them to RP.
3. The RP decapsulates the packet and sends it out the shared tree.
Encapsulated
Data Packet
R
R
RP
Sender 1
DR
R
R

## Slide 52: PIM-SM Source Specific Bypass
DR1
R3
DR2
R
R
Receiver 1
Rendezvous Point (RP)
1. Designated Router DR2 sees traffic from Sender 1 at a rate > threshold. It sends a source specific join request toward Sender 1.
Encapsulated
Data Packet
R
R
RP
Sender 1
DR
R
R
Source Specific Join
Source Specific Join
2. The join request reaches DR1, and DR1 adds DR2 to the source specific tree for Sender 1. Data from Sender 1 begins flowing on the source specific tree to DR2.
3. When DR2 sees traffic from Sender 1 coming from R3, it sends a Source Specific Prune message toward RP. This removes DR2 from the shared tree.
Source
Specific Prune

## Slide 53: RP Joins Source Specific Tree
DR1
R
DR2
R
R
Receiver 1
1. RP sees traffic from Sender 1 at a rate > threshold. It sends source specific join request toward Sender 1.
Encapsulated
Data Packet
R
R
RP
Sender 1
DR
R
R
Source Specific Join
3. When RP sees unencapsulated traffic from Sender 1, it sends a Register Stop message to DR1. DR1 then stops sending encapsulated traffic to RP.
Source Specific Join
Source Specific Join
2. The join request reaches DR1, and DR1 adds RP to the source specific tree for Sender 1. Data from Sender 1 begins flowing on the source specific tree to RP.

## Slide 54: PIM Rendezvous Point (RP)
Requirement
  Different groups map to different RPs
Bootstrap Router (BSR)
  Dynamically elected
  Constructs a set of RP IP addresses based on received Candidate-RP messages
How do routers know RP for a group?
  Bootstrap Router broadcasts Bootstrap message with RP set to PIM
  Hash function on group address maps to an RP

## Slide 55: Problems with PIM
Global broadcasts of all Rendezvous Points
Sensitive to location of RP
No administrative control over multicast traffic; policy controls lacking
Conceived as inter-domain, but now considered intra-domain

## Slide 56: Border Gateway Multicast Protocol (BGMP)
Motivation
  Hierarchy for multicast routing
  Combine design of multicast address allocation and multicast routing
  Inter-domain routing protocols need administrative control of multicast traffic
Scalability issues
  Need to minimize router state
  Need to minimize control messages
  Only send data where it is needed

## Slide 57: Administrative Control of Traffic
IBM
Intel
Stanford
University
ISP 1
ISP 2
NTT
1. The shortest path from Intel to the Stanford University goes through IBM. However, IBM does not want to act as a transit network for multicast data sent by Intel over its networks.
2. IBM installs an administrative policy that does not propagate any multicast routes of Intel senders in outside of IBM’s internal network.

## Slide 58: Choosing a Shared Tree Root
IBM
Intel
Stanford
University
ISP 1
ISP 2
BBN
3. If Host Z at the Stanford University initiates a conference, the root of the shared tree should be in the Stanford University domain (e.g. Router B). The shared tree only develops in places with interested receivers downstream.
A
B
2. Therefore, the Rendezvous Point for a session started by Host Z at the Stanford University might be in BBN at Router A. The PIM shared tree would cross ISP 2 even though there are no receivers in that direction.
Y
Z
1. Using PIM, the Rendezvous Point for the multicast group is chosen by a hash function on the multicast group.

## Slide 59: Multicast Address Allocation
Problem
  Multicast addresses are a limited resource
  Current multicast address allocation scheme does not scale and makes multicast routing more difficult
Solution
  Use dynamically allocated addresses
  Address allocation location determines root of shared tree
  Hierarchical address allocation scales better and helps multicast routing

## Slide 60: Multicast Address Allocation Architecture
Multicast Address Set Claim (MASC)
  Protocol to allocate multicast address sets to domains
  Algorithm: Listen and claim with collision detection
  Makes hierarchy available to routing infrastructure
Address Allocation Protocol (AAP)
  Protocol for allocating multicast addresses within domains
  Used by Multicast Address Allocation Servers (MAAS)
MDCHP (Multicast DHCP)
  Protocol for end hosts to request multicast address
  Extension to DHCP (Dynamic Host Configuration Protocol)

## Slide 61: Multicast Address Allocation Example
MAAS
MDHCP
MAAS
MDHCP
MAAS
MDHCP
MAAS
MASC
MASC
Multicast AAP
MASC
TCP MASC Exchanges
Allocation Domain

## Slide 62: Address Allocation Message Exchange
Client
Local
MAAS
Server
Remote
MAAS
Server
MASC
Router for
Domain
AAP Address
Set Advertisement
MDHCP address request
AAP Address
Set Advertisement
MDHCP address allocation
AAP address claim
AAP address collide
AAP address claim
AAP timeout
period (eg 2 seconds)
AAP address set near
exhaustion warning
Periodic AAP
address claim
after MASC claim
interval (eg 1 day)
MASC address claim

## Slide 63: BGMP Design
Administrative control of multicast traffic
Hierarchical multicast address allocation
Uses BGP for routing tables
No global broadcasts of anything
Bi-directional shared multicast routing tree

## Slide 64: Border Gateway Protocol (BGP)
Unicast inter-domain routing protocol
Uses path vector routing
Administrative control of traffic
Provides multiple views of network topology
Can accept injected routing information