## Slide 1: The Open Extensible Gateway (OEG)
March 19, 1998
Gordon Chaffee
Berkeley Multimedia Research Center
University of California, Berkeley
Email: chaffee@bmrc.berkeley.edu
URL: http://bmrc.berkeley.edu/people/chaffee

## Slide 2: Outline
Introduction
Gateway Services
Active Networks
Security Issues
OEG Design
Notes: RSVP: The largest part of this talk will focus on RSVP and discuss what it is and how it works.
Emerging network protocols: In addition, I will briefly discuss other new network technologies such as IPV6, IP security, and Mobile iP.
Open Extensible Gateway: I’ll also talk a bit about the open extensible gateway and the issues involved in implementing one.
Testbed Network: Last, I am going to describe the network testbed that we are creating. We will use this network to run experiments with RSVP and gateways.

## Slide 3: What is an OEG?
Toolkit for application specific gateways
  Provides a programming interface for building gateway services
Framework for deploying gateway services
  Provides security/authentication
An Active Networks project
  Custom code is executed in network
  Allows easy network customization

## Slide 4: Why Make Networks Programmable?
Networks already have many specialized services
  Firewalls, web proxies, media translation gateways, agents
Not easy to add new services to network
No common interface . . .
  For creating services
  For deploying new services
Current techniques are ad hoc

## Slide 5: Firewall
Gateway service between Internet and internal network
Filters packets based on a set of rules
Packet firewall
  Stateless
  All decisions based solely on the contents of the packet

## Slide 6: Firewall (cont’d)
Application filtering firewall
  Maintains state of TCP connections passing through it
  Intelligent filtering based on contents of streams
  Can block downloaded programs (e.g. ActiveX, Java, Win32 executables)
Needs periodic updates for new security risks, new application stream types

## Slide 7: Network Address Translation Gateway
Gateway service between private and public networks
Packet level address translation
Application specific modules to handle different application streams
Needs periodic updates for new protocols
Similar to functionality required by firewalls

## Slide 8: Web Proxies
Different requirements for different users
Examples
  Web caches: cache near edges of network
  Offline web cache: cache on user’s machine
  Web advertisement filters: filter on user’s machine
  Web gateway: private to public network service
User stream programmability
Stream (transport) level service

## Slide 9: Media Translation Gateways
Translate specific media streams from one format or size to another
Translators placed at network boundaries
Examples
  vgw: Video Gateway converts RTP video streams
  Image distillation: convert images to lower resolution at gateway
Desire to dynamically place into network

## Slide 10: Agents
Mobile code pieces
Need to move entire execution state from node to node
  Require support for code mobility

## Slide 11: Other Gateway Services
End-to-end principal
  Put functionality where it is required, but allow functionality in other locations as an optimization
Localized optimizations services for wireless networks
  Selecting layered multimedia streams
  SNOOP protocol
  Adding FEC information to data stream

## Slide 12: Selecting Layered Multimedia Streams
R
R
1 Mb/s
1 Mb/s
1 Mb/s
512 Kb/s
1 Mb/s
Sender
Receiver 1
BS
128 Kb/s
In Receiver-driven Layered Multicast (RLM), receivers attempt to add layers if there is no congestion
Optimization: Base Station knows maximum capacity of wireless network, does not allow adding additional layers
Result: no congestion caused by receivers adding layers

## Slide 13: SNOOP Protocol
Optimizes TCP data delivery to wireless networks
Function
  Base station caches data that is sent onto wireless network
  Waits for ACK to remove data from cache
  If no ACK before timeout, retransmit data
Server
Internet
Base
Station
Mobile Host

## Slide 14: Active Networks
Organized approach to adding network services
Routers and switches perform customized computation of behalf of user applications
  Packet data can be modified
  Contrasts with receive and forward architecture
Notes: In current networks, routers and switches do not want to add to their processing work. In fact, Gigabit technology does the exact opposite of active networks. It tries to remove as much processing from the network in order to speed up the network and create greater bandwidth.
Routers can do limited processing on packets, but the processing is usually limited to changing IP headers.

## Slide 15: Why Active Networks?
Difficult to add new services to networks
  IP multicast took almost 10 years to get into network
  No resource reservation in network
Accelerate infrastructure innovation
  Network innovation is too slow
Current ad hoc techniques are inadequate for quickly deploying services

## Slide 16: Active Network Approaches
Work within current IP model
  Out-of-band communication between application and routers to install customized code
Define new packet format
  Packet header contains program
  Payload contains data, but program can operate on data
Issues
  Performance, security, easy of use

## Slide 17: Problem Discussion
Need to find a good tradeoff between these feature
  Flexibility
  Security
  Performance
  Usability

## Slide 18: Enabling Technologies
Requirements
  Mobility
  Safety
  Efficiency
Safe programming languages
  Safe-Tcl
  Java
Compilers
  Trustworthy compilers
  Just-in-time compilation
Notes: Safe-Tcl achieves safety thorugh interpretation of a program and closure in its namespace. This prevents programs from purposefully or accidentally executing privileged commands. The primary disadvantage is the speed at which programs run. However, the code is easily read.
Java's runtime environment provides safety with a sandbox environment.
The SPIN project created a trusted compiler. It relies on the properties of the Modula 3 language to generate programs that do not stray from a protected environment.

## Slide 19: Security Issues
Permissions
  Not all users should have same capabilities
  Administrators and trusted users have greater capabilities
  End users should be able to modify their data flows
Safe execution of code
  Protection against intentional and unintentional misuse of router resources
  Need to prevent denial of service

## Slide 20: Security Issues
Flow safety
  Only allow end users to impact their own flows
  Global flow changes require greater permissions
Denial of service
  Need safe resource allocation
  Detection of problem code
Trust
  What trust is needed between gateways?
  Do users need to trust network?
  Does network need to trust users?

## Slide 21: OEG Design
Architecture
Code deployment
Security
Trust

## Slide 22: OEG Architecture Components
Trust module
Scheduler
Packet interceptor
Packet injector
Packet classifier
TCP module
Services

## Slide 23: OEG Architecture Diagram
Packet
Classifier
Packet
Interceptor
Scheduler
Code
Module
Code
Module
Code
Module
Code
Module
Trust
Module
TCP
Module
Packet
Injector
Gateway Service
Gateway Service
Packets
In
Packets
Out

## Slide 24: OEG Trust Module
Concerns
  How can you bind a flow to a particular user?
  Can you get privacy on programmable networks?
  Can a single OEG applet break the router?
Trust Model
  Code signing
    Trusted code has greater rights
    Administrator control
  Neighbor to neighbor trust system

## Slide 25: OEG Trust Establishment
Trust Modules authenticate neighboring OEGs with public key exchanges
  Trust Proxy on routers without OEG
Binds flows to users
  Transitive trust exchange to establish services
Workstation
Router
Router
Workstation
OEG Trust Proxy
OEG
Router
OEG

## Slide 26: OEG Scheduler
Gateway services provide a resource profile
  Profile specifies required resources (CPU, buffers,) storage space, bandwidth
  Provides a way to detect runaway or malicious services
Scheduler switches between different services
  Some services are CPU intensive (e.g. media translation)
Detects and terminates misbehaving services

## Slide 27: OEG Services
OEG hosts multiple services
Downloadable modules
Modules combined into services
Packet Classifier
Image
Xform
FEC Module
Service #1
EncryptionModule
FEC Module
Service #2
Packets In
Packets Out

## Slide 28: OEG Packet Handling
Packet Interceptor and Packet Injector
  Use FreeBSD’s IP Divert facility
  Kernel to user transition adds latency
Packet Classifier
  Binds packets to flows
  Services bound to flow
TCP Module
  Turns packets into streams
  Generates new packets, responds to ACKs

## Slide 29: OEG Deployment
Deploy OEGs at boundaries that have bandwidth differentials
  Wired to wireless networks
  Campus to home connections
Trust Proxies extend reach of trust

## Slide 30: OEG Platform Independence
Desirable to have single code module that can be inserted into OEG by a program
  Easier to build user agents
Use virtual machine
  Java, Lingo languages
  Java VM, Dis
  Aids in security

## Slide 31: OEG Performance
Throughput concerns
  Intelligent processing can be expensive
Virtual machines cause slowdowns
  Java VM has garbage collection
  Dis is better suited for real-time
Provide primitives to aid in expensive operation such as image manipulation