## Slide 1: Networking Overview
March 19, 1998
Gordon Chaffee
Berkeley Multimedia Research Center
University of California, Berkeley
Email: chaffee@bmrc.berkeley.edu
URL: http://bmrc.berkeley.edu/people/chaffee

## Slide 2: Outline
Multicast
Quality of Service
Programmable Networks
Other Networking Issues
Schedule of Talks
Notes: RSVP: The largest part of this talk will focus on RSVP and discuss what it is and how it works.
Emerging network protocols: In addition, I will briefly discuss other new network technologies such as IPV6, IP security, and Mobile iP.
Open Extensible Gateway: I’ll also talk a bit about the open extensible gateway and the issues involved in implementing one.
Testbed Network: Last, I am going to describe the network testbed that we are creating. We will use this network to run experiments with RSVP and gateways.

## Slide 3: Background
IP networks emerged as standard for data communications
Internet was successful research network
Web led to explosive growth of public and commercial use
Computer/communication technology improvements enabled distributed multimedia applications (e.g. video collaboration)

## Slide 4: Application Demand
Audio/video, telephony, collaboration, and distance learning
Data distribution (e.g. news, software, stock ticker, etc)
Radio and television style broadcasting (e.g. RealAudio)
Multicast is essential
Quality of service

## Slide 5: Problems
Demand overwhelms network capacity
IP network model is best effort
  No guarantees on quality of service
Great variability in network technology and service (ATM, Ethernet, wireless)
Users want ubiquitous, reliable, high quality applications and services

## Slide 6: What is multicast?
1 to N communication
Network hardware efficiently supports multicast transport
  Example: Ethernet allows one packet to be received by many hosts
Many different protocols and service models
  Examples: IETF IP Multicast, ATM Multipoint

## Slide 7: Unicast
R
Sender
Problem
  Sending same data to many receivers via unicast is inefficient
Example
  Popular WWW sites become serious bottlenecks

## Slide 8: Multicast
R
Sender
Efficient one to many data distribution

## Slide 9: MBone
In 1992, the MBone was created to further the development of IP multicast
Experimental, global multicast network
Served as a testbed for multicast applications development
  vat -- audio tool
  vic -- video tool
  wb -- shared whiteboard

## Slide 10: MBone Usage
Dramatic increase in use...
  Research: telecollaboration, protocol development
  Learning: conferences, seminars, and classes
  Entertainment: Rolling Stones concert
Leads to much higher bandwidth demand
  Groups range from < 10 to 1000’s, will grow to millions
  Number of programs/groups -- thousands of channels

## Slide 11: Internet Video
Variable bandwidth and quality
  Frame rate, image size, delay
Vary bandwidth and quality depending on receiver demand
  Very large groups can use more/less bandwidth depending on network capabilities and economics
  Small groups on a campus can use very high quality
  Wireless viewers use low bandwidth
Different viewers get different qualities for one program (wireless vs wired computers)

## Slide 12: Video Transmissions
Traditional Internet
Frame rate Fixed Variable
Image size Fixed Variable
Delay Fixed, bounded Variable
Transmissions Analog Digital packets
Signal Noisy Lost packets

## Slide 13: Future of Internet Video
Many video streams share network links
  Need to limit total bandwidth consumed by video
Allocate bandwidth by receiver interest
  SCUBA (Scalable ConsensUs Based Allocation) does this per session
Need a similar mechanism for global allocations
Receivers adapt to signal based on available bandwidth

## Slide 14: RLM Example
R
R
1 Mb/s
1 Mb/s
128 Kb/s
512 Kb/s
1 Mb/s
Sender
Receiver 3
Receiver 2
Receiver 3

## Slide 15: ISP Concerns
Multicast causes high network utilization
  One source can produce high total network load
  Experimental multicast applications are relatively high bandwidth: audio and video
  Flow control non-existent in many multicast apps
Multicast breaks telco/ISP pricing model
  Currently, both sender and receiver pay for bandwidth
  Multicast allows sender to buy less bandwidth while reaching same number of receivers
  Load on ISP network not proportional to source data rate

## Slide 16: Economics of Multicast
One packet sent to multiple receivers
Sender
  + Benefits by reducing network load compared to unicast
  + Lower cost of network connectivity
Network service provider
  - One packet sent can cause load greater than unicast packet load
  + Reduces overall traffic that flows over network
Receiver
  = Same number of packets received as unicast

## Slide 17: Multicast Problems
Multicast is immature
  Tools are poor, difficult to use
  Routing protocols leave many issues unresolved
Multicast development has focused on academic problems, not business concerns
Routing did not address policy
  PIM, DVMRP, CBT do not address ISP policy concerns
  BGMP addresses some ISP concerns, but it is still under development

## Slide 18: Current ISP Multicast Solution
Restrict senders of multicast data
Charge senders to distribute multicast traffic
  Static agreements
Do not forward multicast traffic
  Some ISP’s offer multicast service to customers (e.g. UUNET UUCast)
  ISP beginning to discuss peer agreements

## Slide 19: Multicast Service Model
IP Multicast is an unreliable delivery service

## Slide 20: Reliable Multicast
Some applications need the same data to be delivered reliably to many receivers
  Distributed collaboration tools (e.g. shared whiteboard)
  Stock history
  Software distribution
Status
  Many different proposals
  Proposals solve some problems but have not considered commercial limitations of multicast
  Still exploring applications for reliable multicast

## Slide 21: Real-Time Transport Protocol (RTP)
Transport protocol for real-time data
  Primarily used for audio and video
Provides simple, common services for real-time data
  Additional services provided by profile and payload format
No delivery or quality of service guarantees
Status
  Mature protocol being used by some commercial applications
Notes: Works with Unicast and Multicast networking models.
Delivery Guarantees: Ordering, etc

## Slide 22: Future Directions
Approaches to improve applications and networks for distributed multimedia
  Make applications more adaptive
  Make protocols more resilient to loss
  Make algorithms more resilient to loss
  Make networks more responsive and flexible

## Slide 23: Adaptive Applications
Flexible handling of lost and late data
Lost data should lead to loss of fidelity but not usefulness (i.e. degraded audio quality)
Increase, decrease bandwidth usage in response to changing network conditions

## Slide 24: Loss Tolerant Protocols
Minimize dependencies between packets
  Application data units can be operated on independently
No fragmentation of data packets
Use forward error correction (FEC) for data delivery

## Slide 25: Loss Tolerant Algorithms
Use source encoding algorithms to generate network friendly data
Modify existing algorithms
  Intra H.261 is a subset of H.261 without inter-frame dependencies
Receiver driven layered multicast (RLM)

## Slide 26: Future of IP Networks
Today, IP networks treated as black boxes
Future
  Make networks more responsive
  Make networks more predictable
  Give users more control over networks
Methods
  Explicit congestion notification
  Integrated Services, RSVP, Differentiated Services
  Programmable networks (Active Networks, application-specific gateways)

## Slide 27: Quality of Service Approaches
Integrated Services/RSVP
  Fine resource allocations
Differential
  Coarse resource allocations
The real question is to choose which packets shall be dropped. The
first definition of differential service is something like "not mine.”
-- Christian Huitema

## Slide 28: Integrated Services
Complex model for allocating resources
Make networks predictable and controllable
Different applications can request different delivery services
Uses RSVP reservation protocol
Tries to solve many hard problems
  End-to-end admission control
  End-to-end pricing

## Slide 29: ReSeverVation Protocol (RSVP)
Signaling protocol for Integrated Services
Fine grain control of network bandwidth
End-to-end solution, but requires support in network
  Difficult to implement incrementally
Complicated solution
Flow management does not scale to backbones

## Slide 30: Differentiated Services
Simple, lightweight solution for resource allocation
Intended to operate on aggregated flows
  Should scale to backbone networks
Contrasts with Integrated Services/RSVP
  Int-Serv/RSVP tried to solve every resource allocation problem on an end-to-end basis
  Diff-Serv only specifies per-hop behavior

## Slide 31: Differentiated Services
Domain 2
Domain 3
Domain 1
BR
Costly work at border/edge routers
  Traffic shaping, policing, priority re-marking
Internal routers use simple priority queuing
Behaviors
  Per-hop behavior defined (within domain)
  End-to-end behavior undefined (across domains)
BR
BR
BR

## Slide 32: Active Networks
Routers and switches perform customized computation on behalf of user applications
  Packet data can be modified
  Contrasts with receive and forward architecture
Why?
  Difficult to add new services to networks
    IP multicast took almost 10 years to get into network
    No resource reservation in network
  Accelerate infrastructure innovation
    Network innovation is too slow
Notes: In current networks, routers and switches do not want to add to their processing work. In fact, Gigabit technology does the exact opposite of active networks. It tries to remove as much processing from the network in order to speed up the network and create greater bandwidth.
Routers can do limited processing on packets, but the processing is usually limited to changing IP headers.

## Slide 33: Active Network Approaches
Work within current IP model
  Out-of-band communication between application and routers to install customized code
Define new packet format
  Packet header contains program
  Payload contains data, but program can operate on data
Issues
  Performance, security, easy of use

## Slide 34: Open Extensible Gateway (OEG) “Toolkit for Application Specific Gateways”
Gateways run variety of services
  Services usually implemented independently
No way to dynamically add new gateway services
OEG defines a toolkit to build and deploy gateway services
Out of band service deployment
  Similar to RSVP

## Slide 35: Other Networking Issues
Internet’s rapid growth raised concern that there are not enough IP addresses
  Led to development of Classless Inter-Domain Routing (CIDR) and Network Address Translation (NAT)
Companies want to build private networks using the public Internet
  Led to the development of Virtual Private Networks (VPN)

## Slide 36: IP Address Depletion
Addresses divided into classes
  Class A: 256 addresses (195.199.1.*)
  Class B: 65536 addresses (128.32.*.*)
  Class C: 2^24 addresses (18.*.*.*)
Not enough block sizes to reflect network needs

## Slide 37: Network Address Translation (NAT)
Allows privately addressed networks to function on Internet
Requires at most a few IP addresses per network, reducing global IP address demand
Other uses
  Better site security
  Load balancing web servers
  Load balancing networks

## Slide 38: Virtual Private Networks (VPN)
Simple definition
  A VPN is a private network constructed within the public Internet
Construct logical network from networks at remote locations
Add remote users to home network
Using shared infrastructure reduces cost of building networks

## Slide 39: Outline of Presentations
Today
  IP multicast and basic multicast routing
  Real-time protocol, receiver driven layered multicast, and reliable multicast
  Open Extensible Gateway
Tomorrow
  ReSerVation Protocol (RSVP) and Integrated Services
  Differentiated Services
  Multicast routing protocols (CBT, PIM, BGMP)
  Virtual Private Networks and Network Address Translation