## Slide 1: RTP, Reliable Multicast, and RLM
March 19, 1998
Gordon Chaffee
Berkeley Multimedia Research Center
University of California, Berkeley
Email: chaffee@bmrc.berkeley.edu
URL: http://bmrc.berkeley.edu/people/chaffee

## Slide 2: Outline
RTP: The Real-Time Transport Protocol
RLM: Receiver Driven Layered Multicast
Reliable Multicast
SRM: Scalable Reliable Multicast
Notes: RSVP: The largest part of this talk will focus on RSVP and discuss what it is and how it works.
Emerging network protocols: In addition, I will briefly discuss other new network technologies such as IPV6, IP security, and Mobile iP.
Open Extensible Gateway: I’ll also talk a bit about the open extensible gateway and the issues involved in implementing one.
Testbed Network: Last, I am going to describe the network testbed that we are creating. We will use this network to run experiments with RSVP and gateways.

## Slide 3: RTP Overview
Transport protocol for real-time data
  Primarily used for audio and video
Network independent (IP, ATM, etc)
Services provided
  Payload type identification
  Payload independent sequence numbering
  Payload dependent timestamping
  Out of band control/information/feedback channel
Services not provided
  Delivery, QoS guarantees
Notes: Works with Unicast and Multicast networking models.
Delivery Guarantees: Ordering, etc

## Slide 4: Principles
Lightweight Sessions
  No centralized group membership control
Application Level Framing (ALF)
  Guideline for defining application protocols

## Slide 5: Lightweight Sessions Model
No explicit control of group membership
  Participants just join multicast group
No explicit conference control
Members with data send it
Quasi-periodic session packets
  Identity, reception reports, synchronization info
Fits well with multicast model
Contrasts with H.320 session protocol

## Slide 6: Application Level Framing (ALF) Clark and Tennenhouse, 1990 (MIT)
Clark and Tennenhouse, 1990
Application semantics reflected in the communication protocol
  Do not put functions where they are not universally needed
  TCP semantics do not always reflect application needs
    Application might not need reliability
    Application might not need in order delivery

## Slide 7: ALF (cont’d)
Vertical design: design protocols across layers
Application
Link
Layer
Network
Layer
Application
Link
Layer
Network Layer
Network
Constraint: Link layer packet maximum packet size 1500 bytes
Constraint: Network loses packets
Transport
Layer
Transport
Layer

## Slide 8: ALF (cont’d)
Application controls packetization
Create idempotent Application Data Units (ADUs)
  Each ADU can be processed independently
Fit ADUs into single network packet (if possible)

## Slide 9: ALF Example
Video
Frame
Video
Frame
Video
Frame
Video
Frame
Video
Frame
Video
Frame
Video
Frame
IP Packet
IP Packet
IP Packet
IP Packet
IP Packet
Application ignores network framing (i.e. TCP)
Application frames data to fit into network layer packets (i.e. UDP without fragmentation)
Video
Frame 1
IP Packet
Video
Frame 2
IP Packet
Video
Frame 3
IP Packet
Video
Frame 4
IP Packet
Video
Frame 5
IP Packet
Video
Frame 6
IP Packet
Video
Frame 7
IP Packet

## Slide 10: Joint Source/Channel Coding
Principle
  Corollary to ALF
  It is important to account for the transmission channel when designing a source coding algorithm
Network aware source coding algorithm
  Modify algorithms to produce idempotent data
  Loss of packet has little impact

## Slide 11: Standard H.261 Algorithm
Block transform algorithm
  Similar to JPEG, MPEG
  Precursor to H.263+
Predictive system
  Differential encoding between frame N and frame N-1
  Motion compensated blocks
Assumes non-lossy channel (e.g. ISDN)
If data loss...
  Resynchronizes on next Group of Blocks (GOB)
  Reconstruction errors persist in decoder

## Slide 12: Standard H.261 Example
+
Decode
Predictive System
Encode
Decode
+
Transmission Medium
-
Output
Frame
Reference
Frame
Reference
Frame
Input
Frame
1. Compute difference between Input Frame blocks and Reference Frame blocks
2. Encode differences between blocks using DCT and quantization
3. Send encoded difference data over transmission medium. H.261 assumes the transmission medium is serial and not lossy. If loss occurs, H.261 does not work well.
+
4. Decode difference and add to reference frame to compute Output Frame. Output Frame is now the new Reference Frame.

## Slide 13: Intra H.261 Algorithm
IP network aware
Subset of H.261
Conditional replenishment
No differential updates across frames
Macroblocks form ADUs

## Slide 14: Intra H.261 Example
+
> Threshold?
Encode
Decode
Conditional Replenishment System
Reference
Frame
-
Transmission Medium
3. Send encoded blocks over transmission medium. Intra H.261 assumes the transmission medium may lose data packets.
1. Compute difference between input frame blocks and reference frame blocks
2. Encode entire blocks if difference between blocks exceeds a certain threshold. Like H.261, Intra H.261 uses the DCT for encoding.
4. Decode encoded blocks directly into Output Frame. Note that there are no dependencies on prior frames.

## Slide 15: RTP Components
RTP
  Data channel
RTCP
  Control and information channel

## Slide 16: RTP
General framework for data delivery
ALF principal reflected in hierarchical structure
  Requires profile (such as Audio-Video)
  Requires payload format (mpeg, mjpeg, H.261, pcm)
Extensible headers
RTP
A/V
Profile
MPEG
Video
Layered
Video
H.261
Video
PCM
Audio
LPC
Video
PVH
Video
LDCT
Video
HVQ
Video

## Slide 17: RTP Packet Header
Sequence Number
Payload Format
Version
Padding
Extension
Marker
Contributing
Source
Count
Timestamp
Synchronization Source Identifier (SSRC)
Contributing Source Identifier (CSRC)
. . . .
Optional Header Extension
Monotonically
Increasing
Media
Specific
Original Source or
Mixer Identifier
Mixers may
combine multiple
senders
Notes: Find some examples of specific Payload Types

## Slide 18: RTP Control Protocol (RTCP)
Feedback/Information channel
Announce-Listen protocol
Soft-state
Tracks participants using sender and receiver reports
Monitors quality of data delivery
Provides for stream synchronization

## Slide 19: RTCP Scalability
Uses 5% of session bandwidth
  Shared by all participants
  25% allocated to senders
  75% allocated to receivers
Scaling characteristics
  Reports sent periodically with random delay
  Period based on estimated number of participants
RTP Data
Traffic (95%)
RTCP Control
Traffic (5%)
Receiver messages (75%)
Sender messages (25%)
Notes: 5% is not absolute, but it is the recommended value. A specific profile can use a different percentage. Similarly, the 25/75 split is not absolute.
Potential problems:
If many receivers join at nearly the same time, the estimate of the number of session participants can be too low. This can cause too much bandwidth to be used by congestion reports. A way to deal with this problem is with timer reconsideration. This says to only send a receiver report if the estimate of the number of participants has not increased since the timer was last set.
In very large sessions, it may be difficult to get an accurate count because receiver reports will be so few and far between. It becomes difficult to know when session participants have left the session. By aggregating receiver reports, it might be easier to provide more and better information in the same bandwidth.

## Slide 20: RTCP Example
Receiver Reports contain this information

## Slide 21: RTCP Transmission Interval
Interval dependent on number of members
Counting session members
  Table entry for each new RTP source identifier seen
  Member marked inactive after 5 intervals without a new message
  Do not remove from table in case of network partitions
Source description (SDES) bandwidth allocation
  Send some information frequently (e.g. name)
  Send other information less frequently (e.g. email address)

## Slide 22: RTCP Messages
Required for multicast transmissions
  Diagnostic tool
  Control feedback can cause sender to change send rate
Packet types
  RR: Receiver Report
  SR: Sender Report
  SDES: Source Description
  BYE: End of Participation
  APP: Application Specific
Notes: In a Unicast transmission, loss rate can be used directly to slow sending rate or to decide how much error recovery information to send along with data.
Reception reports can be useful to the sender as a method to determine whether a problem is local or global. Can also be used by network management tools to find problems.

## Slide 23: RTCP Sender Report
V=2
P
Reception
Report Count
Packet Type=SR=200
Length
Synchronization Source Identifier (SSRC) of Sender
NTP Timestamp, Most Significant Word
NTP Timestamp, Least Significant Word
RTP Timestamp
Sender’s Packet Count
Sender’s Octet Count
Header
Sender Info
Maps format
specific timestamp
to wall clock time.
Used to synchronize
different media
streams.
Report Blocks and Profile Specific Extensions
Report Blocks
Report blocks used
in both Sender and
Receiver Reports

## Slide 24: RTCP Reception Report Blocks
Cumulative Number of Packets Lost
Extended Highest Sequence Number Received
Interarrival Jitter
Last Sender Report (LSR)
Delay Since Last Sender Report (DLSR)
Synchronization Source Identifier 1 (SSRC_1)
Fraction Lost
Synchronization Source Identifier 2 (SSRC_2)
. . .

## Slide 25: RTCP Discussion
Receiver and sender reports are combined
Receiver report includes statistics on every sender received in the last period
Scaling problems
  Many receivers joining at nearly the same time
  No aggregation of reports

## Slide 26: Debugging RTP Sessions
rtpmon
  Collects Receiver Reports
  Displays receiver statistics
rtpdump
  Dumps RTP data and control messages

## Slide 27: Receiver-driven Layered Multicast (RLM)
Heterogeneous network means different bandwidths needed by each user
  One multicast group equals one identical stream for all, but heterogeneous receivers want different bitrate flows
Use source/channel coding with layered transmission
  Code signal into N layers
  Transmit each layer on different multicast address
  Receiver joins multiple channels if bandwidth available
Notes: With only a single multicast group, a sender can only send a single data stream. Therefore, the sender has to send to the least common denominator if there is a heterogeneou audience.

## Slide 28: RLM Example
R
R
1 Mb/s
1 Mb/s
128 Kb/s
512 Kb/s
1 Mb/s
Sender
Receiver 3
Receiver 2
Receiver 3

## Slide 29: RLM Adaptation
Receivers adapt to network conditions
  Join experiments
  Add channel when no congestion (e.g. few lost packets)
  Drop channel if congestion is detected
Receivers share adaptation information
  Broadcast when join experiments begin
  Other receivers wait to conduct their own join experiments
  If other receivers experience additional congestion, they backoff their next join experiment time.

## Slide 30: RLM Adaptation Example
R
R
1 Mb/s
1 Mb/s
128 Kb/s
512 Kb/s
1 Mb/s
Sender
Receiver 3
Receiver 2
Receiver 3
1. Receiver 2 does a join experiment. It adds a layer by joining the layer’s multicast group.
2. Congestion occurs because there is not enough bandwidth to support the added layer.
3. Receiver 2 detects the congestion and drops the added layer. The join experiment has failed.

## Slide 31: RLM Join Experiments
Join experiments help determine optimal bandwidth usage
How often should experiments be done?
  Failed experiments cause congestion
  Wish to avoid congestion as much as possible
Useful to look at TCP congestion control algorithm

## Slide 32: RLM Congestion Control
Linear increase, multiplicative decrease is difficult with few layers
Solution
  Failed experiments cause congestion
  Exponential backoff on start time of next join experiment
  All receivers in loss region share same experiment

## Slide 33: Receiver-driven Bandwidth Adaptation for Light-weight Sessions
Elan Amir, Steven McCanne, and Randy Katz (UC Berkeley)
Methods for controlling bandwidth usage
  Fixed rate (no congestion control)
  Sender-based congestion control (e.g. IVS)
  Receiver-based congestion control (e.g. RLM)
All schemes account for network dynamics
but not interaction dynamics (“focus”).

## Slide 34: Distributed Classroom Scenario
MBone

## Slide 35: Distributed Classroom Scenario
MBone

## Slide 36: Distributed Classroom Scenario
MBone

## Slide 37: SCUBA: A Scalable ConsensUs-based Bandwidth Adaptation Protocol
Multimedia conference sources are not of all equal interest to the receiver!
A mechanism that complements existing rate-control schemes by reflecting receiver interests in partitioning of available bandwidth.
S0
S2
S1
R3
R2
R1
R0
S0
S1
S0
S0

## Slide 38: SCUBA: An Announce/Listen Protocol
Periodic self-descriptive messages (“soft state”).
Receivers announce source weights.
Sources listen and aggregate to form an average source weight.
Average source weight is input to source’s rate-controller as a parameter in determining transmission rate.
Rj
S2
S1
S0
{w0,w1,w2}
{w0,w1,w2}
{w0,w1,w2}
Rj
S2
S1
S0
S2
S1
S0
S2
S1
S0
S2
S1
S0
{w0,w1,w2}
{w0,w1,w2}
{w0,w1,w2}
{w0,w1,w2}
{w0,w1,w2}
{w0,w1,w2}
{w0,w1,w2}
{w0,w1,w2}
{w0,w1,w2}
Rj
Rj
Rj

## Slide 39: SCUBA Source Weighting
Source signal is sent on single network channel with aggregate total bandwidth B.
Map average source weight, wk, to transmission rate, Bk, in straightforward way:
Refine above scheme with 95/5 rule:

## Slide 40: Scalability Issues
Report message size scales linearly with number of active sources
  Solution: Limit number of sources in each report to small constant number.
Control traffic scales linearly with number of reporting receivers.
  Solution: maintain fixed control traffic bandwidth allocation
Source-weight convergence time, t, scales linearly with number of reporting receivers, N:
  Solution: sampling.
Result: 20-25 kb/s of control traffic allocation are sufficient for low worst case convergence time (<10 sec) with tight confidence bounds (>95%) independent of session size.

## Slide 41: Reliable Multicast
Build reliability on top of unreliable multicast
Extending TCP to multicast works poorly
  Positive acknowledgement
  Sliding window
  Sender keeps state for each receiver
NAK

## Slide 42: TCP Sliding Window Flow Control
Controls bandwidth usage (bw = win/RTT)
Controls amount of data sender must hold
Window moves forward on ACK of data
Sender holds state about receiver
Sender
Receiver
ACK
Data Packet

## Slide 43: Reliable Multicast Problems
Need to control feedback
  Naive ACK and NAK based schemes cause implosions
Want to limit how long sender holds data
  In some schemes, perfect reliability leads to infinite storage requirements
Sender cannot make resource decisions
  No single RTT or bandwidth to all receivers
Scalability of state in senders and receivers
Scalability of control/recovery traffic

## Slide 44: Reliable Multicast Considerations
Number of receivers
Data lifetime
  Data delivery must be timely
  Different types of data have different useful lifetimes

## Slide 45: Reliable Multicast Techniques
Log-based recovery
Receiver initiated loss recovery with NAK suppression
Hierarchical recovery
Forward Error Correction (FEC)

## Slide 46: Log-based Recovery
Some hosts store data indefinitely
If receivers drop packets, they contact one of the log hosts via unicast or multicast
Data can live forever
Issues
  Limiting recovery traffic
  Length of time to store data

## Slide 47: Receiver Initiated, NAK Suppression
Announce-Listen protocol
Receivers randomly delay NAK, suppress NAK if another receiver has already sent one
Used in Scalable Reliable Multicast (SRM)
Problems
  NAK schemes never move the window forward
  In large groups, data may need multiple retransmissions

## Slide 48: Hierarchical Recovery
Organize receivers into tree-based groups
In local groups, members send ACKs or NAKs to group leader
Group leaders send ACKs or NAKs up tree
Issues
  How to organize?
  State requirements for ACK trees

## Slide 49: Forward Error Correction
Send data with correcting codes
If any k out of n packets in a group are received, all data can be recovered
Reduces the number of required resends
Can use separate FEC multicast channels or send in band
Data lifetime can determine how FEC info is used

## Slide 50: Reliable Multicast Transport Protocol (RMTP)
Receivers divided into groups
Single shared ACK tree
Each group has a Designated Receiver (DR)
Periodic local ACKs
DR aggregates ACKs
Sender receives few ACKs
Statically configured currently

## Slide 51: Scalable Reliable Multicast (SRM)
General framework for reliable data distribution
1st implemented in LBL shared whiteboard, wb
Receiver initiated, NAK suppression
Collaborative error recovery
  Receivers request retransmission missing data by multicasting to group
  Any receiver with data can retransmit
End-to-end solution (no network intelligence)

## Slide 52: SRM Framework
Application Level Framing
Lightweight Sessions
  No distinction between senders and receivers
  Session control channel similar to RTCP
  Source identifiers are persistent
  Users can leave/join sessions without losing identity
All data has a unique, persistent name
Focus on reliability, not congestion control
  Reliability needed by many applications
  Congestion control differs based on application

## Slide 53: SRM Session Messages
Report sequence number state per sender
Bandwidth limited to 5% of total bandwidth
Sent periodically with random delay
  Chosen from interval [.5 * period, 1.5 * period]
Determines distances between members
Time = T1
Time = T2
A
B
Time = T4
Time = T3
distance = (T4 - T3 + T2 - T1) / 2

## Slide 54: SRM Loss Recovery
Receiver initiated recovery with NAK suppresssion
Random delay based on distance from sender

## Slide 55: SRM Local Recovery
Problem: repairs sent to entire group
  Excessive use of bandwidth
Determine loss neighborhood
  Correlate loss found in session messages
Send repairs to sub-group
  Administrative scoping
  Separate multicast groups
  TTL-based scoping

## Slide 56: Local Recovery Example
3. Host B resends the repair it received from Host A with TTL = 2. This ensures that all hosts that heard the original repair request will not respond with an additional repair.
Repair
1. Host B experiences a loss. It determines its loss neighborhood, and it sends a repair request to the multicast group with TTL=2.
Repair
Request
2. Host A has the data that Host B requested, so it sends a repair to the multicast group with TTL=2. This is enough to reach Host B, but not enough to reach Host C.
Repair
B
A
C

## Slide 57: SRM Scalable Session Messages
Problems with session messages
  State maintained for every session member
  Poor estimates with very large number of receivers
Solution: Hierarchical session messages
  Self configuring hierarchy of members
  Based on randomized timers and local appropriateness measure
  Global and local session members

## Slide 58: Scalable Session Messages: Example
Global Representative
Session Member
Each member decides if it should switch to being local or being global based on the number of session messages it received in the last interval

## Slide 59: Problems with SRM
Technical
  Receivers cannot adapt to data flows
  State maintained per receiver
Internet Service Providers
  Deny subscribers ability to send multicast
    Cannot control network utilization
    Sender oriented charging
    Want network load to equal charge
  But... SRM requires everyone to send
    Local recovery
    Receiver reports

## Slide 60: Erasure Correcting SRM
Receiver initiated recovery with NAK suppression and FEC based retransmissions
Reed-Solomon Erasure Correcting Codes
Algorithm
  Packets transmitted in groups
  NAKs contain number of lost packets in group
  Suppress NAK if see another NAK is seen with at least as many lost packets for the group
  Sender sends enough correction packets to recover lost data (i.e. parity if single packet losses throughout net)
Notes: Implemented by Luigi Rizzo

## Slide 61: Erasure Correcting SRM (1)
Group of
Data Blocks
NAK
Count = 1

## Slide 62: Erasure Correcting SRM (2)
Resend Erasure
Correcting Codes
Recovered
Packets