INSTALLATION:

If you received this from HUE (Harris Users' Exchange), you should have
received the following files:

  2000KERM*KERM.DOC  this documentation

  2000KERM*KERMSRV   executable Kermit Server -- rename this to
                     be on the 0SYST* qualifier

  2000KERM*HARRIS    on-line help file giving a brief command summary
                     (must be given Public Read access)

  2000KERM*KERM:J    jobstream used to recompile KERMSRV

  2000KERM*K:SERVE   Fortran source for main program
  2000KERM*K:SEND    Fortran source for sending files (i.e. from Harris)
  2000KERM*K:RECV    Fortran source for receiving files (i.e. to Harris)
  2000KERM*K:COMMND  Fortran source implementing remote commands
  2000KERM*K:DIRECT  Fortran source implementing directory command
  2000KERM*K:UTIL    Fortran source for Kermit protocol primitives
  2000KERM*K:VSUBS   Assembler source for miscellaneous subroutines

Otherwise, if you received this from Columbia University's Kermit tape or by
electronic mail, you will need to compile the source code to create the
KERMSRV program.  In this case you should have received the following files:

  H100KER.DOC  save this as 2000KERM*KERM.DOC
  H100KER.JCL  save this as 2000KERM*KERM:J
  H100KER.F77  save this as 2000KERM*K:SOURCE
  H100KER.ASM  save this as 2000KERM*K:VSUBS
  H100KER.HLP  save this as 2000KERM*HARRIS and give it Public Read access

Once renamed, the files are as described above.  Note that the source files
K:SERVE through K:UTIL are collected together into the single file K:SOURCE.
Simply type "$JS KERM:J" to compile.

------------------------------------------------------------------------

WHAT IT DOES:

     "Kermit" programs are used to transfer files between different
  computers over ordinary serial communications lines.  Kermits in
  various forms exist for almost every type of computer and operating
  system.  One might think of Kermit of as a mutual language by which
  unlike systems can talk with each other.  In order to transfer a file,
  one only needs to start a Kermit on each of the two machines and
  then issue simple Kermit commands to get the transfer started.  Kermit
  has mechanisms to maintain the integrity of data even over noisy phone
  lines where transmissions might otherwise become garbled.

     A true Kermit has the ability to be both a "local Kermit" and a
  "remote kermit".  In any Kermit session, one Kermit is local and the
  other is remote.  In essence, the local Kermit tells the remote kermit
  what to do and the remote kermit obeys, regardless of which direction
  the file is being transferred.  In this regard, KERMSRV is not a true
  Kermit.  KERMSRV operates only as a remote Kermit and thus acts on
  instructions by some other local Kermit.  What consequences does this
  have?  For one, Harris to Harris transfers are not possible using
  KERMSRV on both ends.  For another, KERMSRV cannot be used to call up
  another computer and initiate a file tranfer.  In other words, no
  dial-out Kermit sessions are possible, only dial-in (or direct
  terminal connection) ones.  Furthermore,  all interaction with KERMSRV
  is done only through the local Kermit's "Server" commands.

HOW TO USE IT:

  To begin with, one typically connects to the Harris as if the local
  computer were a terminal, using the terminal emulation capabilities of
  the local Kermit to do so.  After signing on, the user invokes KERMSRV
  on the Harris, whereupon the following message will be displayed:

      SERVER MODE ENABLED -- type the appropriate key
      sequence to escape back to your local Kermit...

  The exact key sequence to type depends on the particular version of
  (local) Kermit being used.  For instance, in the case of MS-Kermit
  on the IBM PC under DOS, one would type a <ctrl>] followed by a "c"
  to exit terminal emulation and return to command level of MS-Kermit.

  Once back at command level, one can SEND or GET files, or perform
  various other operations using "server" commands.  To get a short
  summary of the server commands which are implemented, try the
  command "remote help".

------------------------------------------------------------------------

EXAMPLE:

  To illustrate the use of KERMSRV, I will describe the procedure that
  Sam, an IBM PC user, might use to transfer files.  The details when
  using other Kermits will differ slightly.

      dialogue                            comments
      --------                            --------

C:> mskermit                        Sam invokes the DOS version of Kermit
                                    on his PC

IBM PC Kermit-MS V2.29  26 May 86

Kermit-MS> set port 1               Sam sets the characteristics of his
                                    communications line with the Harris
Kermit-MS> set baud 9600

Kermit-MS> set parity even

Kermit-MS> connect                  Sam begins terminal emulation
                                    then signs onto the Harris
^G
VOS 5.1.0  WU BIOSTATISTICS
ENTER SIGN-ON
1234SQS SAMMY

** GOOD AFTERNOON SAM, IT'S 22 SEP 1986  13:51:21

KERMSRV                             Sam invokes KERMSRV on the Harris

HARRIS KERMIT SERVER  --  version 1.02 (Sept 86) SR

[logging names of send/receive files to LO]


SERVER MODE ENABLED -- type the appropriate key
sequence to escape back to your local Kermit...

^]c                                 Sam types control/] followed by the
                                    letter "C" to get back to MSKERMIT
                                    (may be different in other Kermits)

Kermit-MS> REM HELP                 Sam requests a summary of commands
                                    that he can use
 . . .

Kermit-MS> GET                      Sam prepares to transfer a file from
                                    the Harris to the PC
 Remote Source File: 1234QUAL*TEXTFILE
 Local Destination File: A:TXT.FIL

   receiving: in progress
 . . .
   receiving: completed

Kermit-MS> SEND                     Sam prepares to tranfer a file from
                                    the PC to the Harris
 Local Source File: PC.FIL
 Remote Destination File: HARFILE

   sending: in progress
 . . .
   sending: completed

Kermit-MS> REM HELP                 Sam forgot how to quit, so he asks
                                    for another command summary
 . . .

Kermit-MS> BYE                      Sam logs off the Harris and exits
                                    back to DOS
C:>

      [end of dialogue]

------------------------------------------------------------------------

SUMMARY OF FEATURES IMPLEMENTED AND NOT IMPLEMENTED IN VERSION 1.06

      what it can do:

            remote operation
            transfer 7 bit ascii (text) files
            transfer file groups via wildcard send/get
            on-line help
            on-line directory information about files or file groups
            remote shutdown or logout
            debugging option to log packet traffic

      what it can't do:

            local operation
            terminal emulation
            8th bit prefixing
            repeat count processing
            extended block check types
            JCL (host) commands

------------------------------------------------------------------------

WILDCARD COMMANDS:

  the wildcard character "?" can be used in the GET and REMOTE DIR
  commands to operate on groups of files.  KERMSRV will attempt to
  match all disk areanames where ? replaces any substring of zero or
  more characters.  For example, GET ?OO? will get the files OO,
  FOO, BALOON, and any others containing "OO".  REMOTE DIR A? will
  return directory information on all areanames in the current
  qualifier beginning with the letter "A".

------------------------------------------------------------------------

TECHNICAL NOTES:

  This program, KERMSRV, was born of my need to transfer files between
  our aging Harris 100 and an IBM PC.  It implements the "server"
  portion of the "Kermit" protocol, as described in version 3 of the
  protocol manual (see reference below).

  I wrote this program especially for Harris computers which are
  configured with a "MUX" as opposed to the more recent CNP or DMACP
  I/O processors, since the Pascal-based Harris Kermit which was already
  in existence does not accommodate such a configuration.  As such, I
  have not taken advantage of many of the special features offered by
  those devices (notably timeouts and buffered I/O via "hot read"),
  but have opted instead for simpler, albeit less efficient, modes
  of communication.  In any case, this program should work properly
  on a Harris machine in any configuration.

  Specifically, incoming packets are read using symbolic input mode
  rather than binary input mode.  (For details of these modes, see
  the VOS I/O services manual under "TTY functions codes".)  Binary
  mode would have been desirable in that it gives the ability to read
  one character at a time.  However, without using "hot read" for
  buffering, binary reads are not fast enough to keep up at higher
  baud rates.  Since hot I/O is not available on MUX based systems,
  we have to settle for the record-at-a-time symbolic input mode, and
  leave the buffering to VOS.  The two biggest ramifications are
  (1) abort and other control characters cannot be trapped and
  processed individually, and (2) the size of the input buffer is
  fixed at system generation time, and is often set to 80 characters,
  regardless of the size of the buffer used in the $I/O call.


------------------------------------------------------------------------

REVISION HISTORY:

  This program was written using Harris Fortran 77 on a Harris H100-1
  computer (VOS 4.1.1 operating system).  It was tested at up to 9600
  baud against Columbia University's "MSKERMIT" version 2.27 (see below)
  on an IBM PC/AT running DOS 3.0.  I wrote the first version of
  KERMSRV in January, 1986

  version 1.00  Jan, 1986, by Skip Russell : initial release

  version 1.01  Feb, 1986, by S.R. :
     brought up to version 5 of the protocol manual (dated April 1984)
     and tested using MSKERMIT version 2.28; also implemented the
     following remote commands:
        -- HELP command to issue summary of available remote commands
        -- LOGOUT ("bye") command to log off the Harris job
        -- DIRECTORY command to issue information about a single disk
           area (for now; plan to add wildcard match in future)

  version 1.02  Sept, 1986, by S.R. :
     -- implemented full DIRECTORY command (wildcard character "?")
     -- tested using MSKERMIT version 2.29 (dated 26 May 86)
     -- moved to non-SAU Fortran 77 compiler for portablity

  version 1.03  Nov, 1986, by S.R. :
     -- brought up to VOS 5.1.0 (required changes in interpretation of
        file access bits in "REMOTE DIRECTORY" command handler)
     -- fixed logic in RECVSW to correctly respond to error packets

  version 1.04  April, 1987, by S.R. :
     -- added code to allow GETs of file groups using the "?" wildcard
        character.

  version 1.05  May, 1987, by S.R. :
     -- Corrected error in SWOPEN.  GETs of file groups failed in
        cases where the qualifier contained trailing blanks.  The fix
        consisted of enclosing the file name in quotes.

  version 1.06  June, 1987, by S.R. :
     -- Added code in RDISK to distinguish between EOF and EOT.  Harris
        disk areas containing embedded EOFs can now be sent without
        truncating trailing records.  The EOF is sent as a record
        containing the string "<EOF>".

------------------------------------------------------------------------

BEWARES:

-- Many Harris systems treat the XOFF or control-S character as
   an abort character.  If this is the case with your system, ensure
   that flow control is turned off by the local Kermit before
   transferring files.

-- IBM PC users using MS-Kermit version 2.29 or 2.29a should note
   that when flow-control is turned off, a NULL character is
   substituted for the XOFF.  Unfortunately, this is also an abort
   character on many Harris systems.  Transfers can usually be made
   to work by using a RAM disk (VDISK) on the PC or lower baud rates
   to avoid buffer overflows, while keeping flow-control on.

-- MS-Kermit 2.29a and 2.29b (IBM PC under DOS) had a bug where packets
   of 94 characters were sent despite the request by KERMSRV to limit
   the packet size to 80.  The fix is to manually set the send packet-
   length to 80.  (This has been fixed in MS-Kermit 2.30)

------------------------------------------------------------------------

REFERENCES

  For a complete discussion of the Kermit design philosophy and
  detailed descriptions of Kermit commands, see the "KERMIT USER'S
  GUIDE" by Frank da Cruz, Daphne Tzoar, and Bill Catchings.

  For a detailed description of the Kermit protocol, see the
  "KERMIT PROTOCOL MANUAL" by Frank da Cruz and Bill Catchings.

  These two documents, as well as general information about Kermit,
  MSKERMIT and other implementations of Kermit for almost any type
  of computer or operating system, are available for the cost of
  distribution, from:

     KERMIT Distribution
     Columbia University Center for Computing Activities
     612 West 115th Street
     7th Floor
     New York, NY  10025

  or send electronic mail to: Info-Kermit-Request@CU20B.ARPA

------------------------------------------------------------------------

  This document was last revised on February 25, 1988

  Skip Russell
  Division of Biostatistics
  Washington University in St. Louis
  electronic mail address: c04689sr@WUVMD.BITNET